## Slide 1
Chapter 2
Boolean Arithmetic
From Nand to Tetris
Building a Modern Computer from First Principles
These slides support chapter 2 of the book
The Elements of Computing Systems
(1st and 2nd editions)
By Noam Nisan and Shimon Schocken
MIT Press

## Slide 2: Usage Notice
  You are welcome to use this presentation, or any part of it, in Nand to Tetris courses, or in other courses, as you see fit.
  Usage is free provided that it supports instruction in educational, non-profit settings.
  You can use the slides as-is, or modify them as needed.
  We’ll appreciate it if you will credit Nand to Tetris somewhere, and put a reference to www.nand2tetris.org
  Happy teaching!
  Shimon Schocken / Noam Nisan

## Slide 3: Nand to Tetris Roadmap: Hardware
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p2
p3
p4
p5
p6

## Slide 4: Nand to Tetris Roadmap: Hardware
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p2
p3
p4
p5
p6
Project 1
Build 15 elementary logic gates

## Slide 5: Nand to Tetris Roadmap: Hardware
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p2
p3
p4
p5
p6
Project 2
Building chips that do arithmetic, ending up with an ALU

## Slide 6: Computer system
Input
Memory
Output
CPU
Registers
ALU

## Slide 7: Computer system
Input
Memory
Output
CPU
ALU
Registers

## Slide 8: Arithmetic Logical Unit
ALU
f
(x, y)
x
y
f
The ALU computes a given function on two given n-bit values, and outputs an n-bit value
ALU functions (f)
Arithmetic: x + y, x – y, x + 1, x – 1, ...
Logical: x & y, x | y, !x , ...

## Slide 9: Arithmetic Logical Unit
ALU
+
1001111001001001
0000000000010001
(40521)
(17)
1001111001011010
(40538)
ALU functions (f)
Arithmetic: x + y, x – y, x + 1, x – 1, ...
Logical: x & y, x | y, !x , ...
Challenges
Use 0’s and 1’s for representing numbers
Use logic gates for realizing arithmetic functions.
The ALU computes a given function on two given n-bit values, and outputs an n-bit value

## Slide 10: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Signed numbers

## Slide 11: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Signed numbers

## Slide 12: Representation
This is not a pipe
(by René Magritte)

## Slide 13: Representation
17
This is not seventeen.
Rather, it’s an agreed-upon code (numeral)
that represents the number seventeen.

## Slide 14: A brief history of numeral systems
Twenty seven goats
Unary:
Roman:
XXVII
Egyptian:

## Slide 15: A brief history of numeral systems
Old numeral systems:
Don’t scale
Cumbersome arithmetic
Used until about 1000 years ago
Blocked the progress of Algebra (and commerce, science, technology)
Unary:
. . .
Roman:
MMMMMMDVII
Egyptian:
. . .
Six thousands, five hundreds, and seven goats

## Slide 16: Positional numeral system
Where n is the number of digits in the numeral, and di is the digit in position i
6 5 0 7
6507
3
2
1
0
A most important innovation, brought to the West from the East around 1200
Positional representation
Digits: A fixed set of symbols, including 0
Base: The number of symbols
Numeral: An ordered sequence of digits
Value: The digit in position i (counting from right to left, and starting at 0) encodes how many copies of basei are added to the value.
The method mentions no specific base.
. . .
Six thousands, five hundreds, and seven goats

## Slide 17: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Representing signed numbers

## Slide 18: Positional number system
7053
3
2
1
0
7 0 5 310
. . .
Seven thousands and fifty three goats

## Slide 19: Positional number system
1 1 0 1 1 1 0 0 0 1 1 0 12
7053
. . .
3
2
1
0
12
11
10
. . .
7 0 5 310
7053
3
2
1
0
. . .
Seven thousands and fifty three goats
Decimal (base 10) system:
Human friendly
Binary (base 2) system:
Computer friendly

## Slide 20: Binary and decimal systems
0
1
1 0
1 1
1 0 0
1 0 1
1 1 0
1 1 1
1 0 0 0
1 0 0 1
1 0 1 0
1 0 1 1
1 1 0 0
1 1 0 1
...
Binary
Decimal
0
1
2
3
4
5
6
7
8
9
10
11
12
13
...
Humans are used to enter and view numbers in base 10;
Computers represent and process numbers in base 2;
Therefore, we need efficient algorithms for converting from one base to the other.

## Slide 21: Decimal binary conversions

## Slide 22: Decimal binary conversions
543210
binary (
5310) =
Decimal to binary:
decimal (
1101012
(
Binary to decimal:
5310
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
. . .
Powers of 2: (aids in calculations)
1101012
543210
Algorithm: What is the largest power of 2 that “fits into” 53? It’s 32 = 25. We still have to handle 53 – 32, so, what is the largest power of 2 that fits into 21? It’s 16 = 24, and so on.
Practice:
decimal (
10110102
(
binary (
52310
(

## Slide 23: Decimal binary conversions
543210
binary (
5310) =
Decimal to binary:
decimal (
1101012
(
Binary to decimal:
5310
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
. . .
Powers of 2: (aids in calculations)
1101012
543210
Algorithm: What is the largest power of 2 that “fits into” 53? It’s 32 = 25. We still have to handle 53 – 32, so, what is the largest power of 2 that fits into 21? It’s 16 = 24, and so on.
Practice:
decimal (
10110102
(
binary (
52310
(
9010
10000010112

## Slide 24: The binary system
G.W. Leibnitz (1646 – 1716)
Worshipped binary numbers
Inside computers, everything is binary
Binary numerals are easy to:
Compare
Add
Subtract
Multiply
Divide
...
Store
Transmit
Verify
Correct
Compress
...

## Slide 25: Chapter 2: Boolean Arithmetic
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Signed numbers
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines

## Slide 26: Boolean arithmetic
Addition
Subtraction
Multiplication
Division
We have to figure out efficient ways to perform, on binary numbers:
We’ll implement it using logic gates
Based on addition
We’ll get it for free
Addition is the foundation of all arithmetic operations.

## Slide 27: Addition
1
3
7
5
7
8
6
2
5
+
Decimal addition
1
4
1
0
1
0
1
1
+
Binary addition
7
0
8
0
0
1
1
0
1
0
1
0

## Slide 28: Addition
1
0
1
0
1
1
+
Binary addition
0
1
1
0
1
0
1
0

## Slide 29: Addition
1
0
1
0
1
1
0
0
1
0
1
1
1
+
Binary addition
Computers represent integers using a fixed number of bits, sometimes called “word size”. For example, let’s assume n = 4:
0
0
0
Another example
0
1
0
0
0
1
0
1
+

## Slide 30: Addition
1
0
1
0
1
1
0
0
1
0
1
1
1
+
Binary addition
0
0
0
0
1
0
0
0
1
0
1
+
1
1
0
0
1
0
0
Another example
Computers represent integers using a fixed number of bits, sometimes called “word size”. For example, let’s assume n = 4:

## Slide 31: Addition
1
0
1
0
1
1
0
0
1
0
1
1
1
+
Binary addition
0
0
0
0
1
0
0
0
1
0
1
+
1
1
0
0
1
0
0
Another example
1
1
0
1
1
0
1
1
+
Another example
Computers represent integers using a fixed number of bits, sometimes called “word size”. For example, let’s assume n = 4:

## Slide 32: Addition
1
0
1
0
1
1
0
0
1
0
1
1
1
+
Binary addition
0
0
0
1
1
0
1
1
0
1
1
+
Overflow
1
1
1
1
0
1
0
1
0
Handling overflow
Our decision: Ignore it
As we will soon see, ignoring the overflow bit is not a bug, it’s a feature.
0
1
0
0
0
1
0
1
+
1
1
0
0
1
0
0
Another example
Computers represent integers using a fixed number of bits, sometimes called “word size”. For example, let’s assume n = 4:

## Slide 33: Addition
...
0
0
0
...
0
0
0
0
0
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
1
1
0
0
0
0
1
0
0
1
1
1
0
0
0
1
0
0
0
0
0
1
0
0
1
1
0
0
0
1
0
0
+
...
...
Hardware implementation
We’ll build an Adder chip that implements this addition algorithm,
Using the chips built in project 1.
How? Later.
Word size n = 16, 32, 64, …
Same addition algorithm for any n
Teaching Note
In Nand to Tetris we always separate abstraction from implementation
First we present the abstraction, leaving the implementation to a later stage in the lecture.

## Slide 34: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic (addition)
  Signed numbers

## Slide 35: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic (addition)
  Signed numbers
(x + y, –x + y, x + –y, –x + –y)

## Slide 36: Signed integers
Teaching Note
Designers of low-level hardware / software systems use numerous ingenious hacks for optimizing arithmetic operations, memory manipulations, graphics, signal processing, and other mission critical computer operations.
The Two’s Complement method is a simple and powerful example of this art.
Instead of building different chips for handling, say, addition and subtraction, we choose to represent signed numbers cleverly. The representation allows us to use the same Adder chips for doing addition, subtraction, and mixed sign arithmetic.
The result – often taken for granted – is one of the most dramatic optimizations in computer processing.
This triumph of human reasoning over physical work is therefore worth teaching and celebrating.

## Slide 37: Signed integers
Therefore …
Efficient algorithms for handling arithmetic operations on signed integers hold the key to building efficient computers.
Positive
0
Negative
In most programming languages, the short, int, and long data types use 16, 32, and 64 bits for representing signed integers
Arithmetic operations on signed integers (x op y, –x op y, x op –y, –x op –y, where op = {+, –, *, /}) are by far what computers do most of the time
Teaching Note: All the algorithms presented in this course can be implemented efficiently in either hardware of software.

## Slide 38: Signed integers
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 8
1001 9 9
1010 10 10
1011 11 11
1100 12 12
1101 13 13
1110 14 14
1111 15 15
code(x)
x
This particular example: word size is n = 4
In general, n bits allow representing all the unsigned integers 0 … 2n – 1
What about negative numbers?
We can use half of the code space for representing positive numbers, and the other half for negatives.

## Slide 39: Signed integers
Issues
– 0: Huh?
code(x) + code(– x) ≠ code(0)
The codes are not monotonically increasing
more complications.
Representation:
Left-most bit (MSB): Represents the sign, +/-
Remaining bits: Represent a positive integer
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 0
1001 9 – 1
1010 10 – 2
1011 11 – 3
1100 12 – 4
1101 13 – 5
1110 14 – 6
1111 15 – 7
code(x)
x

## Slide 40: Two’s complement
The representation
Assumption: Word size = n bits
The “two’s complement” of x is defined to be 2n – x
The negative of x is coded by the two’s complement of x
if x ≥ 0 return binary(x)
else return binary(2n – x)
From decimal to binary:
if MSB = 0 return decimal(bits)
else return “–” and then (2n – decimal(bits))
From binary to decimal:
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x

## Slide 41: Two’s complement: Addition
6
–2
+
20
6
14
+
=
% 16 = 4
codes 4
3
–5
+
14
3
11
+
=
% 16 = 14
codes –2
–2
–5
+
25
14
11
+
=
% 16 = 9
codes –7
Algorithm: Regular addition, modulo 2n
Compute x + y where x and y are signed
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x

## Slide 42: Two’s complement: Addition
6
–2
+
20
6
14
+
=
% 16 = 4
codes 4
Algorithm: Regular addition, modulo 2n
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
Practice:
4
–7
+
–2
–4
+
=
=
Compute x + y where x and y are signed

## Slide 43: Two’s complement: Addition
6
–2
+
20
6
14
+
=
% 16 = 4
codes 4
Algorithm: Regular addition, modulo 2n
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
Practice:
4
–7
+
13
4
9
+
=
% 16 = 13
codes –3
14
12
+
26
% 16 = 10
codes –6
–2
–4
+
=
Compute x + y where x and y are signed

## Slide 44: Two’s complement: Addition
6
–2
+
10100
0110
1110
+
=
codes 4
3
–5
+
1110
0011
1011
+
=
codes –2
–2
–5
+
11001
  1110
1011
+
=
codes –7
At the binary level (same algorithm):
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
Ignoring the overflow bit is the binary equivalent of modulo 2n

## Slide 45: Two’s complement: Addition
6
–2
+
10100
0110
1110
+
=
codes 4
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
5
7
+
1100
0101
0111
+
=
codes –4
–7
–3
+
10110
  1001
1101
+
=
codes 6
More examples:
Overflow detection
When you add up two positives (negatives) and get a negative (positive) result, you know that you have overflow
5 + 7 = –4 ???
–7 + –3 = 6 ???
At the binary level (same algorithm):

## Slide 46: Two’s complement: Subtraction
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
x – y is the same as x + (–y)
So… convert y and add up the two values (we already know how to add up signed numbers)
Compute x – y where x and y are signed
But … How to convert a number (efficiently)?

## Slide 47: Two’s complement: Sign conversion
Algorithm: To convert bbb...b:
Flip all the bits and add 1 to the result
Compute –x from x
= 1 + (1111) – x
code(–x) = (2n – x)
Insight:
= 1 + (2n – 1) – x
= 1 + flippedBits(x)
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
1101 (flipped)
1110 (–2)
1
+
Example: Convert 0010 (2)

## Slide 48: Two’s complement: Sign conversion
Algorithm: To convert bbb...b:
Flip all the bits and add 1 to the result
Compute –x from x
= 1 + (1111) – x
code(–x) = (2n – x)
Insight:
= 1 + (2n – 1) – x
= 1 + flippedBits(x)
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
Practice: Convert 1010 (–6)

## Slide 49: Two’s complement: Sign conversion
Algorithm: To convert bbb...b:
Flip all the bits and add 1 to the result
Compute –x from x
= 1 + (1111) – x
code(–x) = (2n – x)
Insight:
= 1 + (2n – 1) – x
= 1 + flippedBits(x)
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x
0101 (flipped)
0110 (6)
1
+
Practice: Convert 1010 (–6)

## Slide 50: Two’s complement: Recap
Observations
The method represents all the integers in the range –2n–1, ..., –1, 0, 1, ..., 2n–1 – 1
code(x) + code(– x) = code(0)
The codes are monotonically increasing
Arithmetic on signed integers is the same as arithmetic on unsigned integers
Simple! Elegant! Powerful!
Implications for hardware designers
Arithmetic on signed integers can be implemented using the same hardware used for handling arithmetic of unsigned integers
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 – 8
1001 9 – 7
1010 10 – 6
1011 11 – 5
1100 12 – 4
1101 13 – 3
1110 14 – 2
1111 15 – 1
code(x)
x

## Slide 51: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Signed numbers

## Slide 52: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Signed numbers

## Slide 53: Von Neumann Architecture
Input
Memory
Output
CPU
Registers
ALU
Computer System

## Slide 54: The Arithmetic Logical Unit
ALU
f
(input1, input2)
input1
input2
f
f
: one out of a family of pre-defined arithmetic functions (add, subtract, multiply…) and logical functions (And, Or, Xor, …)
The ALU computes a given function on its two given data inputs, and outputs the result
Design issue: Which functions should the ALU perform?
A hardware / software tradeoff: Any function not implemented by the ALU can be implemented later in system software
Hardware implementations: Faster, and more expensive
Software implementations: Slower, less expensive

## Slide 55: The Hack ALU
Operates on two 16-bit, two’s complement values

## Slide 56: The Hack ALU
Operates on two 16-bit, two’s complement values
Outputs a 16-bit, two’s complement value
out
0
1
-1
x
y
!x
!y
-x
-y
x+1
y+1
x-1
y-1
x+y
x-y
y-x
x&y
x¦y

## Slide 57: The Hack ALU
Operates on two 16-bit, two’s complement values
Outputs a 16-bit, two’s complement value
Also outputs two 1-bit values (later)
out
0
1
-1
x
y
!x
!y
-x
-y
x+1
y+1
x-1
y-1
x+y
x-y
y-x
x&y
x¦y

## Slide 58: The Hack ALU
Operates on two 16-bit, two’s complement values
Outputs a 16-bit, two’s complement value
Also outputs two 1-bit values (later)
Which function to compute is set by six 1-bit inputs
out
0
1
-1
x
y
!x
!y
-x
-y
x+1
y+1
x-1
y-1
x+y
x-y
y-x
x&y
x¦y

## Slide 59: The Hack ALU
To cause the ALU to compute a function:
Set the control bits to one of the binary combinations listed in the table.
zx | nx | zy | ny | f | no | out
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
control bits

## Slide 60: The Hack ALU in action
zx | nx | zy | ny | f | no | out
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
To cause the ALU to compute a function:
Set the control bits to one of the binary combinations listed in the table.
control bits

## Slide 61: The Hack ALU in action: Compute y-x
zx | nx | zy | ny | f | no | out
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
To cause the ALU to compute a function:
Set the control bits to one of the binary combinations listed in the table.
control bits

## Slide 62: The Hack ALU in action: Compute y-x
Load
tools/builtInChips/ALU.hdl
2. Evaluate the chip logic
3. Inspect the ALU outputs
Set the ALU’s inputs and control bits to some test values
(000111 codes “output y-x”)
The built-in ALU implementation has GUI side-effects
Built-in ALU implementation

## Slide 63: The Hack ALU in action
zx | nx | zy | ny | f | no | out
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
To cause the ALU to compute a function:
Set the control bits to one of the binary combinations listed in the table.
control bits

## Slide 64: The Hack ALU in action: Compute x & y
zx | nx | zy | ny | f | no | out
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
To cause the ALU to compute a function:
Set the control bits to one of the binary combinations listed in the table.
control bits

## Slide 65: The Hack ALU in action: Compute x & y
Set the ALU’s inputs and control bits to some test values
(000000 codes “compute x&y”)
Inspect the ALU outputs
Set to binary I/O format

## Slide 66: The Hack ALU operation

## Slide 67: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 68: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 69: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 70: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 71: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 72: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y

## Slide 73: The Hack ALU operation: Compute !x
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute !x
x: 1 1 0 0
y: 1 0 1 1 (irrelevant)

## Slide 74: The Hack ALU operation: Compute !x
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute !x
x: 1 1 0 0
y: 1 0 1 1 (irrelevant)
Following pre-setting:
x: 1 1 0 0
y: 1 1 1 1
Computation and post-setting:
x&y: 1 1 0 0
!(x&y): 0 0 1 1 (!x)

## Slide 75: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y

## Slide 76: The Hack ALU operation: Compute y-x
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute y-x
x: 0 0 1 0 (2)
y: 0 1 1 1 (7)

## Slide 77: The Hack ALU operation: Compute y-x
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute y-x
x: 0 0 1 0 (2)
y: 0 1 1 1 (7)
Following pre-setting:
x: 0 0 1 0
y: 1 0 0 0
Computation and post-setting:
x+y: 1 0 1 0
!(x+y): 0 1 0 1 (5)

## Slide 78: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y

## Slide 79: The Hack ALU operation: Compute x|y
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Practice:
See if you get
0 1 1 1 (bitwise Or)
Example: compute x|y
x: 0 1 0 1
y: 0 0 1 1

## Slide 80: The Hack ALU operation: Compute x|y
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute x|y
x: 0 1 0 1
y: 0 0 1 1
Following pre-setting:
x: 1 0 1 0
y: 1 1 0 0
Computation and post-setting:
x&y: 1 0 0 0
!(x&y): 0 1 1 1
Practice:
See if you get
0 1 1 1 (bitwise Or)

## Slide 81: The Hack ALU operation
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y

## Slide 82: The Hack ALU operation: Compute y-1
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute y-1
x: 0 1 0 1 (irrelevant)
y: 0 1 1 0 (6)
Practice:
See if you get
0 1 0 1 (5)

## Slide 83: The Hack ALU operation: Compute y-1
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute y-1
x: 0 1 0 1 (irrelevant)
y: 0 1 1 0 (6)
Following pre-setting:
x: 1 1 1 1
y: 0 1 1 0
Computation and post-setting:
x+y: 0 1 0 1
x+y: 0 1 0 1 (5)
Practice:
See if you get
0 1 0 1 (5)

## Slide 84: The Hack ALU operation
if (out == 0) then zr = 1, else zr = 0
if (out < 0) then ng = 1, else ng = 0
The zr and ng output bits will come into play when we’ll build the complete CPU architecture, later in the course.
One more detail:

## Slide 85: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Signed numbers

## Slide 86: Project 2
Given: All the chips built in Project 1
HalfAdder
FullAdder
Add16
Inc16
ALU
Goal: Build the chips:

## Slide 87: Half Adder
a | b | sum | carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
/** Computes the sum of two bits. */
CHIP HalfAdder {
IN a, b;
OUT sum, carry;
PARTS:
// Put your code here:
}
HalfAdder.hdl
Implementation tip
Can be built from two gates built in project 1.

## Slide 88: Full Adder
Implementation tip
Can be built from two half-adders.
/** Computes the sum of three bits. */
CHIP FullAdder {
IN a, b, c;
OUT sum, carry;
PARTS:
// Put your code here:
}
FullAdder.hdl
a | b | c | sum | carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 89: 16-bit adder
/* Adds two 16-bit, two’s-complement values. The most-significant carry bit is ignored. */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
// Put you code here:
}
Add16.hdl
The bitwise additions are done in parallel
The carry propagation is sequential
Yet… it works fine, as is. How? Stay tuned for chapter 3.
Implementation note
If you need to set a pin x to 0 (or 1) in HDL, use: x = false (or x = true)

## Slide 90: 16-bit incrementor
Inc16.hdl
Implementation:
Simple.
/** Outputs in + 1. */
CHIP Inc16 {
IN in[16];
OUT out[16];
PARTS:
// Put you code here:
}

## Slide 91: ALU

## Slide 92: ALU
/** The ALU */
ALU.hdl

## Slide 93: ALU
ALU.hdl
/** The ALU */
// Manipulates the x and y inputs as follows:
// if (zx == 1) sets x = 0 // 16-bit true
// if (nx == 1) sets x = !x // 16-bit Not
// if (zy == 1) sets y = 0 // 16-bit true
// if (ny == 1) sets y = !y // 16-bit Not
// if (f == 1) sets out = x + y // 2's-complement addition
// if (f == 0) sets out = x & y // 16-bit And
// if (no == 1) sets out = !out // 16-bit Not
// if (out == 0) sets zr = 1 // 1-bit true
// if (out < 0) sets ng = 1 // 1-bit true
...

## Slide 94: ALU
ALU.hdl
Implementation tips
We need logic for:
Implementing “if bit == 0/1” conditions
Setting a 16-bit value to 0000000000000000
Setting a 16-bit value to 1111111111111111
Negating a 16-bit value (bitwise)
Computing Add and Or on two 16-bit values
Implementation strategy
Start by building an ALU that computes out
Next, extend it to also compute zr and ng.
/** The ALU */
// Manipulates the x and y inputs as follows:
// if (zx == 1) sets x = 0 // 16-bit true
// if (nx == 1) sets x = !x // 16-bit Not
// if (zy == 1) sets y = 0 // 16-bit true
// if (ny == 1) sets y = !y // 16-bit Not
// if (f == 1) sets out = x + y // 2's-complement addition
// if (f == 0) sets out = x & y // 16-bit And
// if (no == 1) sets out = !out // 16-bit Not
// if (out == 0) sets zr = 1 // 1-bit true
// if (out < 0) sets ng = 1 // 1-bit true
...

## Slide 95: Relevant bus tips
Using multi-bit truth / false constants:
...
// Suppose that x, y, z are 8-bit bus-pins:
5
4
7
6
1
0
3
2
x:
y:
z:

## Slide 96: Relevant bus tips
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
5
4
7
6
1
0
3
2
x:
y:
z:
Using multi-bit truth / false constants:

## Slide 97: Relevant bus tips
5
4
7
6
1
0
3
2
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
y:
z:
1
1
1
1
1
1
1
1
x:
Using multi-bit truth / false constants:

## Slide 98: Relevant bus tips
5
4
7
6
1
0
3
2
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
z:
1
1
1
1
1
1
1
1
x:
0
0
0
0
0
0
0
0
y:
Using multi-bit truth / false constants:

## Slide 99: Relevant bus tips
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
Unassigned bits are set to 0
5
4
7
6
1
0
3
2
1
1
1
1
1
1
1
1
x:
0
0
0
0
0
0
0
0
y:
0
0
1
1
1
1
0
1
z:
Using multi-bit truth / false constants:
We can assign values to sub-buses

## Slide 100: Relevant bus tips
Sub-bussing:
We can assign n-bit values to sub-buses, for any n
We can create n-bit bus pins, for any n
/* 16-bit adder */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
CHIP Foo {
IN x[8], y[8], z[16]
OUT out[16]
PARTS
...
Add16 (a[0..7] = x, a[8..15] = y, b = z, out = …);
...
Add16 (a = …, b = …, out[0..3] = t1, out[4..15] = t2);
...
}

## Slide 101: Relevant bus tips
/* 16-bit adder */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
CHIP Foo {
IN x[8], y[8], z[16]
OUT out[16]
PARTS
...
Add16 (a[0..7] = x, a[8..15] = y, b = z, out = …);
...
Add16 (a = …, b = …, out[0..3] = t1, out[4..15] = t2);
...
}
Sub-bussing:
We can assign n-bit values to sub-buses, for any n
We can create n-bit bus pins, for any n
Another example of assigning a multi-bit value to a sub-bus

## Slide 102: Relevant bus tips
/* 16-bit adder */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
CHIP Foo {
IN x[8], y[8], z[16]
OUT out[16]
PARTS
...
Add16 (a[0..7] = x, a[8..15] = y, b = z, out = …);
...
Add16 (a = …, b = …, out[0..3] = t1, out[4..15] = t2);
...
}
Creating an n-bit bus (internal pin)
Sub-bussing:
We can assign n-bit values to sub-buses, for any n
We can create n-bit bus pins, for any n
Another example of assigning a multi-bit value to a sub-bus

## Slide 103: ALU: Recap
“Simplicity is the ultimate sophistication.”
― Leonardo da Vinci
The Hack ALU is:
Simple
Elegant

## Slide 104: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Signed numbers

## Slide 105: Project 2
Given: All the chips built in Project 1
HalfAdder
FullAdder
Add16
Inc16
ALU
Goal: Build the chips:

## Slide 106: Guidelines: www.nand2tetris.org/project02
www.nand2tetris.org

## Slide 107: Resources
Project 2 folder (.hdl, .tst, .cmp files): nand2tetris/projects/02
Tools
  Text editor (for completing the given .hdl stub-files)
  Hardware simulator: nand2tetris/tools
Guides
  Hardware Simulator Tutorial
  HDL Guide
  Hack Chip Set API

## Slide 108: Chip interfaces: Hack chip set API
Add16 (a= ,b= ,out= );
ALU (x= ,y= ,zx= ,nx= ,zy= ,ny= ,f= ,no= ,out= ,zr= ,ng= );
And16 (a= ,b= ,out= );
And (a= ,b= ,out= );
Aregister (in= ,load= ,out= );
Bit (in= ,load= ,out= );
CPU (inM= ,instruction= ,reset= ,outM= ,writeM= ,addressM= ,pc= );
DFF (in= ,out= );
DMux4Way (in= ,sel= ,a= ,b= ,c= ,d= );
DMux8Way (in= ,sel= ,a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= );
Dmux (in= ,sel= ,a= ,b= );
Dregister (in= ,load= ,out= );
FullAdder (a= ,b= ,c= ,sum= ,carry= );
HalfAdder (a= ,b= ,sum= , carry= );
Inc16 (in= ,out= );
Keyboard (out= );
Memory (in= ,load= ,address= ,out= );
Mux16 (a= ,b= ,sel= ,out= );
Mux4Way16 (a= ,b= ,c= ,d= ,sel= ,out= );
Mux8Way16 (a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= ,sel= ,out= );
Mux8Way (a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= ,sel= ,out= );
Mux (a= ,b= ,sel= ,out= );
Nand (a= ,b= ,out= );
Not16 (in= ,out= );
Not (in= ,out= );
Or16 (a= ,b= ,out= );
Or8Way (in= ,out= );
Or (a= ,b= ,out= );
PC (in= ,load= ,inc= ,reset= ,out= );
PCLoadLogic (cinstr= ,j1= ,j2= ,j3= ,load= ,inc= );
RAM16K (in= ,load= ,address= ,out= );
RAM4K (in= ,load= ,address= ,out= );
RAM512 (in= ,load= ,address= ,out= );
RAM64 (in= ,load= ,address= ,out= );
RAM8 (in= ,load= ,address= ,out= );
Register (in= ,load= ,out= );
ROM32K (address= ,out= );
Screen (in= ,load= ,address= ,out= );
Xor (a= ,b= ,out= );
Open the API in a window, and copy-paste chip signatures into your HDL code, as needed

## Slide 109: Best practice advice (same as project 1)
Implement the chips in the order in which they appear in the project guidelines
If you don’t implement some chips, you can still use their built-in implementations
No need for “helper chips”: Implement / use only the chips we specified
In each chip definition, strive to use as few chip-parts as possible

## Slide 110: Best practice advice
Implement the chips in the order in which they appear in the project guidelines
If you don’t implement some chips, you can still use their built-in implementations
No need for “helper chips”: Implement / use only the chips we specified
In each chip definition, strive to use as few chip-parts as possible
You will have to use chips implemented in Project 1;
For efficiency and consistency’s sake, use their built-in versions, rather than your own HDL implementations.
That’s It!
Go Do Project 2!

## Slide 111: Chapter 2: Boolean Arithmetic
  Practice
  Arithmetic Logic Unit (ALU)
  Project 2: Chips
  Project 2: Guidelines
  Theory
  Representing numbers
  Binary numbers
  Boolean arithmetic
  Representing signed numbers

## Slide 112: What’s next?
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p2
p3
p4
p5
p6
This lecture / chapter / project:
Build the computer’s ALU

## Slide 113: What’s next?
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p2
p3
p4
p5
p6
Next lecture / chapter / project:
Build the computer’s RAM
This lecture / chapter / project:
Build the computer’s ALU