## Slide 1
Chapter 3
Memory
From Nand to Tetris
Building a Modern Computer from First Principles
These slides support chapter 3 of the book
The Elements of Computing Systems
(1st and 2nd editions)
By Noam Nisan and Shimon Schocken
MIT Press

## Slide 2: Usage Notice
  You are welcome to use this presentation, or any part of it, in Nand to Tetris courses, or in other courses, as you see fit.
  Usage is free provided that it supports instruction in educational, non-profit settings.
  You can use the slides as-is, or modify them as needed.
  We’ll appreciate it if you will credit Nand to Tetris somewhere, and put a reference to www.nand2tetris.org
  Happy teaching!
  Shimon Schocken / Noam Nisan

## Slide 3: Nand to Tetris Roadmap: Hardware
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p3
p2
p4
p5
p6

## Slide 4: Nand to Tetris Roadmap: Hardware
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p3
p2
p4
p5
p6
Project 1: Build basic logic gates
Project 2: Build the ALU

## Slide 5: Nand to Tetris Roadmap: Hardware
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p3
p2
p4
p5
p6
Project 1: Build basic logic gates
Project 2: Build the ALU
This lecture / chapter / project:
Build the computer’s Memory system

## Slide 6: A common theme in computer science
We present a simple model (the simpler, the better)
We explore the model’s power:
  What the model can do
  What it cannot do
We then extend the model, to make it more powerful
Case in point:
Logic gates.

## Slide 7: Logic gates
Model: And, Or, Not, …
Simple, and powerful:
Logic gates can realize any Boolean function, and can be combined to form powerful chips, like an ALU
But, as a general model of computation, logic gates fall short
Limitations
Logic gates cannot store information (bits) over time
Feedback loops are not allowed: A chip’s output cannot serve as its input
Logic gates can handle only inputs of a fixed size. For example, we can build an Or3 gate, and an Or4 gate, and so on, but we cannot build a single gate that computes Or for any given number of inputs
Extension
Allow logic gates to be sensitive to the progression of time.

## Slide 8: Time-independent logic
So far we ignored time
The chip’s inputs were just “sitting there” – fixed and unchanging
The chip’s output was a function (“combination”) of the current inputs, and the current inputs only
ALU
+
0101
1000
1101

## Slide 9: Time-independent logic
So far we ignored time
The chip’s inputs were just “sitting there” – fixed and unchanging
The chip’s output was a function (“combination”) of the current inputs, and the current inputs only
This style of gate logic is sometimes called:
  time-independent logic
  combinational logic
All the chips that we discussed and developed so far were combinational
ALU
+
0101
1000
1101
ALU: The “topmost” combinational chip

## Slide 10: Hello, time

## Slide 11: Hello, time
Software needs:
x = 17
Example (variables):
for i in range(0, 10):
print(i)
Example (iteration):
The hardware must handle the physical time delays associated with computing and moving data from one chip to another.
Hardware needs:
The hardware must be able to remember things, over time:
The hardware must be able to do things, one at a time (sequentially):

## Slide 12: Hello, time
The hardware must handle the physical time delays associated with computing and moving data from one chip to another.
Hardware needs:
ALU
+
5
8
13
Now compute
7 + 11 ...
It will take some time before 7 and 11 will settle down in the input ports, and before the sum 7 + 11 will stabilize. Till then, the ALU will output nonsense.
Software needs:
x = 17
Example (variables):
for i in range(0, 10):
print(i)
Example (iteration):
The hardware must be able to remember things, over time:
The hardware must be able to do things, one at a time (sequentially):

## Slide 13: Hello, time
cycle length
Clock:
tick
tock
Clock:
time-step:
Solution: We can neutralize the time delays if we decide to use discrete time

## Slide 14: Hello, time
Solution: We can neutralize the time delays if we decide to use discrete time
Set the cycle length to be slightly > than the maximum time delay, and…
Decide to use the chips’s outputs only at the end of cycles (time-steps), ignoring what happens within cycles
Details later.
cycle length
Chip’s input:
Chip’s output:
Clock:
tick
tock
Clock:
a
f(a)
b
f(b)
c
f(c)
d
f(d)
e
f(e)
time-step:
As it turns out, the clock can also be used to help implementing chips that behave like memory devices.

## Slide 15: Memory
Memory is time-based:
We remember now what was committed to memory earlier.
Memory: The faculty of the brain by which data or information is encoded, stored, and retrieved when needed.
It is the retention of information over time for the purpose of influencing future action (Wikipedia)
Notes: Talk about mathematical functions, and variables, and lack of time in math

## Slide 16: Memory
loading
x = 21
(cycles)
1 2 3 4 5 6 7 205 206 207 208 209 210 211 ...
time
...
loading
x = 17
storing
, 17, 17, 17, 17, 17, 17, ... ,
storing
, 21, 21, 21, 21, 21, 21, ...
The challenge: Building chips that realize this functionality.
Basic abstractions:
“Loading” a value
“Storing” a value
Register
in
16
out
16
load
Notes: Unlike the DFF, which remembers only the bit from the previous time unit.

## Slide 17: Memory
1-bit
register
Bit
Data
Flip-Flop
DFF
0
1
n-1
...
Register
RAM
RAMn
Register
Register
multi-bit register
...
Register
Bit
Bit
Bit
?
DFF
The challenge: Building chips that realize this functionality.

## Slide 18: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 19: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 20: Representing time
physical time:
Arrow of time:
Continuous

## Slide 21: Representing time
1
0
clock:
physical time:
Arrow of time:
Continuous

## Slide 22: Representing time
1
0
clock:
time: 1 2 3 4 5 . . .
physical time:
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another

## Slide 23: Chip behavior over time (example: Not gate)
1
0
clock:
time: 1 2 3 4 5 . . .
physical time:
(example)
in:
0
1
0
1
out:
(Not(in))
Arrow of time:
Continuous
in:
(arbitrary values)
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another

## Slide 24: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
in:
(arbitrary values)
(example)
out:
(Not(in))
Desired / idealized behavior of the in and out signals:
That’s how we want the hardware to behave
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another

## Slide 25: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
(example)
Arrow of time:
Continuous
out:
(Not(in))
in:
(arbitrary values)
Actual behavior of the in and out signals:
Influenced by physical time delays
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another

## Slide 26: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
(example)
Time delays
Propagation delays
Computation delays
out:
(Not(in))
in:
(arbitrary values)
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another
Cycle length

## Slide 27: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
Cycle length
Design parameter
Set to be slightly > max(time delays)
(example)
out:
(Not(in))
Time delays
Propagation delays
Computation delays
in:
(arbitrary values)
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another

## Slide 28: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
Resulting effect:
Combinational chips react “immediately” to their inputs
Facilitated by the decision to track changes only at cycle ends
out:
(Not(in))
(example)
in:
(arbitrary values)
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another

## Slide 29: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 30: Clock

## Slide 31: Clock: Simulated implementation
Interactive simulation
A clock icon can be used to generate a sequence of tick-tock signals: 0, 0+, 1, 1+, 2, 2+, 3, 3+, ...

## Slide 32: Clock: Simulated implementation
...
// Sets inputs, advances the clock, and
// writes output values as it goes along.
set in 19,
set load 1,
tick,
output,
tock,
output,
tick, tock,
output,
...
Interactive simulation
A clock icon can be used to generate a sequence of tick-tock signals: 0, 0+, 1, 1+, 2, 2+, 3, 3+, ...
Script-based simulation
“tick” and “tock” commands can be used to advance the clock:

## Slide 33: Clock: Physical implementation
Physical clock
An oscillator is used to deliver an ongoing train of “tick/tock” signals
“1 MHz electronic oscillator circuit which uses the resonant properties of an internal quartz crystal to control the frequency. Provides the clock signal for digital devices such as computers.” (Wikipedia)
The oscillator’s output is connected to all the time-based (clocked) chips in the computer
Chip diagram convention:
A triangle icon represents a clock signal input

## Slide 34: Chapter 3: Memory
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines

## Slide 35: Combinational logic / Sequential logic

## Slide 36: Combinational logic / Sequential logic
Combinational logic:
The output depends on the current inputs
The clock is used to stabilize outputs

## Slide 37: Combinational logic / Sequential logic
Combinational logic:
Sequential logic:
The output depends on the current inputs
The clock is used to stabilize outputs
f(a,b)
f(b,c)
f(c,d)
f(d,e)
The output depends on:
Previous inputs
Current inputs (optionally)
This behavior can be used to build chips designed to maintain state: Registers.

## Slide 38: Registers
Input
Memory
(many registers)
Output
CPU
Registers
ALU
Computer Architecture
(a few)

## Slide 39: Registers
Designed to:
“Store” / “remember” / “maintain” / “persist” a value , until...
“Instructed” to “load”, and then “store”, another value.
out
in
load
Bit
1-bit register
Register
in
w
out
w
load
multi-bit register
x = 17, 17, 17, 17, 17, 17, 17, ..., 17
x = 21, 21, 21, 21, 21, 21, ..., 21
time:
loading
maintaining state
loading
maintaining state
Notes: Unlike the DFF, which remembers only the bit from the previous time unit.

## Slide 40: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)

## Slide 41: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
examples of arbitrary input values
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)

## Slide 42: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 43: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 44: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 45: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 46: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 47: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 48: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 49: 1-Bit Register
out:
in:
load:
0
1
0
1
1
0
time:
1
2
3
4
5
6
7
8
“storing”
“storing”
“loading”
“loading”
Resulting behavior:
out
in
load
Bit
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
examples of arbitrary input values

## Slide 50: 1-Bit Register
To read:
probe out
(out always emits the register’s state)
To write:
set in = v
set load = 1
Result: The register’s state becomes v; From the next time-step onward, out will emit v
out
in
load
Bit
Usage:
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)

## Slide 51: Multi-bit Register
Register
in
w
out
w
load
if load(t – 1) then out(t ) = in(t – 1)
else out(t) = out(t – 1)
Load / store behavior: Exactly the same as a 1-bit register
Read / write usage: Exactly the same as a 1-bit register
We’ll focus on word width w = 16, without loss of generality

## Slide 52: Chapter 3: Memory
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines

## Slide 53: Computer architecture
Input
Memory
(RAM)
Output
CPU
Registers
ALU

## Slide 54: RAM
Abstraction: A sequence of n addressable, w-bit registers, with addresses 0 to n-1
Word width: Typically 16, 32, 64 bits (Hack computer: w = 16)
Register
0
1
n-1
...
RAMn
Register
Register

## Slide 55: RAM
Practice question:
Suppose that the RAM size n = 8 registers.
What should be the value of k?
Answer:
k = log2n
out
in
load
w
Register
0
1
n-1
...
RAMn
Register
Register
address
k
Abstraction: A sequence of n addressable, w-bit registers, with addresses 0 to n-1
Word width: Typically 16, 32, 64 bits (Hack computer: w = 16)
w

## Slide 56: RAM
If load == 0, the RAM maintains its state
If load == 1, RAM[address] is set to the value of in
The loaded value will be emitted by out from the next time-step (cycle) onward, until the next load
out
in
load
w
Register
0
1
n-1
...
RAMn
Register
Register
address
k
)Only one RAM register is selected; All the other registers are not affected(
(out always emits the value of RAM[i])
Usage:
To read register i :
set address = i,
probe out
To write v in register i :
set address = i,
set in = v,
set load = 1
Result: RAM[i] ← v
From the next time-step onward, out will emit v
Behavior
w

## Slide 57: RAM
out
in
load
w
Register
0
1
n-1
...
RAMn
Register
Register
address
k
Why “Random Access Memory”?
Irrespective of the RAM size (n), every randomly selected register can be accessed “instantaneously”, at more or less the same speed.
w

## Slide 58: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 59: Computer architecture
Input
Memory
Output
CPU
Registers
ALU
One of the CPU registers acts as a “program counter”

## Slide 60: Counter
Later in the course (chapter 5), we will see that the computer must keep track of which instruction should be fetched and executed next
This task is regulated by a register typically called Program Counter
We’ll use the PC to store the address of the instruction that should be fetched and executed next

## Slide 61: Counter
Later in the course (chapter 5), we will see that the computer must keep track of which instruction should be fetched and executed next
This task is regulated by a register typically called Program Counter
We’ll use the PC to store the address of the instruction that should be fetched and executed next
The PC should support three abstractions:
  Reset: fetch the first instruction
  Next: fetch the next instruction
  Goto: fetch instruction n
PC = 0
PC++
PC = n

## Slide 62: Counter
if reset(t) out(t + 1) = 0
else if load(t) out(t + 1) = in(t)
else if inc(t) out(t + 1) = out(t) + 1
else out(t + 1) = out(t)
PC (counter)
in
16
out
16
load
inc
reset

## Slide 63: Counter
To read:
probe out
To reset:
assert reset,
set the other control bits to 0
To count:
assert inc,
set the other control bits to 0
To set:
set in to v,
assert load,
set the other control bits to 0
Usage:
if reset(t) out(t + 1) = 0
else if load(t) out(t + 1) = in(t)
else if inc(t) out(t + 1) = out(t) + 1
else out(t + 1) = out(t)
PC (counter)
in
16
out
16
load
inc
reset

## Slide 64: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 65: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 66: DFF
examples of arbitrary inputs
1
2
3
4
5
6
7
8
time:
0
1
1
0
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 67: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 68: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 69: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 70: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 71: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 72: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 73: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 74: From DFF to a 1-bit register
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
How can we “load” and then “maintain” a value (0 or 1) over time, without having to feed the value in every cycle?
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 75: From DFF to a 1-bit register
We have to realize a “loading” behavior and a ”storing” behavior, and be able to select between these two states
out(t) = in(t – 1)
out
in
DFF
How can we “load” and then “maintain” a value (0 or 1) over time, without having to feed the value in every cycle?

## Slide 76: From DFF to a 1-bit register
if load(t – 1) then
out(t ) = in(t – 1)
else
out(t) = out(t – 1)
Behavior
if load == 1 the register’s value becomes in
else the register maintains its current value
in
load
out
DFF
1-bit Register
Stores one bit over time
We have to realize a “loading” behavior and a ”storing” behavior, and be able to select between these two states

## Slide 77: Register
if load(t – 1) then
out(t ) = in(t – 1)
else
out(t) = out(t – 1)
in
load
out
DFF
1-bit Register
Stores one bit over time
Bit

## Slide 78: Register
if load(t – 1) then
out(t ) = in(t – 1)
else
out(t) = out(t – 1)
load
out
in
1-bit Register
Stores one bit over time
zoom out...

## Slide 79: Register
if load(t – 1) then
out(t ) = in(t – 1)
else
out(t) = out(t – 1)
load
out
in
1-bit Register
Stores one bit over time
w
out
load
w
in
...
w-bit Register:
Stores w bits over time
Partial diagram, showing some of the chip-parts, without connections

## Slide 80: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 81: Memory hierarchy
1-bit
register
Bit
Data
Flip-Flop
DFF
0
1
n-1
...
Register
Random Access Memory
RAMn
Register
Register
16-bit register
...
Register
Bit
Bit
Bit
?
DFF

## Slide 82: Memory hierarchy
1-bit
register
Bit
Data
Flip-Flop
DFF
0
1
n-1
...
Register
RAMn
Register
Register
16-bit register
...
Register
Bit
Bit
Bit
?
DFF
Random Access Memory

## Slide 83: RAM: Abstraction
(out always emits the state of RAM[i])
Usage:
To read register i :
set address = i,
probe out
To write v in register i :
set address = i,
set in = v,
set load = 1
Result: RAM[i] ← v
From the next time-step onward, out emits v
RAM of n registers:

## Slide 84: RAM: Implementation
Register
in
w
load
out
w
Register
in
w
load
out
w
Register
in
w
load
out
w
...
out
w
in
w
address
k
load
RAM of n registers:
Partial diagram, showing some of the chip-parts, without connections

## Slide 85: RAM: Implementation
Register
in
w
load
out
w
Register
in
w
load
out
w
Register
in
w
load
out
w
...
Mux
(n to 1)
Reading: Can be realized using a Mux
out
w
in
w
address
k
load
RAM of n registers:
Partial diagram, showing some of the chip-parts, without connections

## Slide 86: RAM: Implementation
DMux
(1 to n)
Register
in
w
load
out
w
Register
in
w
load
out
w
Register
in
w
load
out
w
...
Mux
(n to 1)
out
w
in
w
address
k
load
RAM of n registers:
Partial diagram, showing some of the chip-parts, without connections
Reading: Can be realized using a Mux
Writing: Can be realized using a DMux
Connections?
You figure it out

## Slide 87: RAM: Implementation
DMux
(1 to n)
Register
in
w
load
out
w
Register
in
w
load
out
w
Register
in
w
load
out
w
...
Mux
(n to 1)
Observations
The addressing/selection/reading logic is combinational
The writing logic is (i) sequential (clocked)
(ii) embedded in the Register logic.
out
w
in
w
address
k
load
RAM of n registers:
Partial diagram, showing some of the chip-parts, without connections

## Slide 88: RAM: Implementation
...
RAM8
Register
Register
Register
...
RAM64
RAM8
RAM8
RAM8
Same technique can be used to implement RAM devices of any size
…
...
RAM512
RAM64
RAM64
RAM64

## Slide 89: Hack RAM
chip name | n | k
RAM8 | 8 | 3
RAM64 | 64 | 6
RAM512 | 512 | 9
RAM4K | 4096 | 12
RAM16K | 16384 | 14
Why these particular RAM chips?
Because that’s what we need for building the Hack computer.
out
in
load
16
Register
0
1
n-1
...
RAMn
Register
Register
address
k
16
A family of 16-bit RAM chips:
Notes: Albert Einstein about achieving maximum functionality with minimum rules.

## Slide 90: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 91: Project 3
Given:
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
Build:
Bit
Register
PC
RAM8
RAM64
RAM512
RAM4K
RAM16K
Why is the DFF built-in?
Teaching note:
It is quite possible to skip completely the discussion of “Why the DFF is built-in” and the subsequent “DFF Implementation” slides.

## Slide 92: DFF implementation
/** Data Flip-flop: out(t) = in(t-1)
* where t is the current time unit. */
CHIP DFF {
IN in;
OUT out;
BUILTIN DFF;
CLOCKED in;
}
Given:
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
Why is the DFF built-in?

## Slide 93: DFF implementation
The DFF gate logic implementation requires, among other things, connecting Nand gates with feedback loops
/** Data Flip-flop: out(t) = in(t-1)
* where t is the current time unit. */
CHIP DFF {
IN in;
OUT out;
BUILTIN DFF;
CLOCKED in;
}
Part of a possible DFF implementation

## Slide 94: DFF implementation
The DFF gate logic implementation requires, among other things, connecting Nand gates with feedback loops
The resulting implementation is elegant, yet impossible to realize on the supplied hardware simulator:
The hardware simulator does not allow loops of combinational chips (like Nand)
Part of a possible DFF implementation
/** Data Flip-flop: out(t) = in(t-1)
* where t is the current time unit. */
CHIP DFF {
IN in;
OUT out;
BUILTIN DFF;
CLOCKED in;
}

## Slide 95: DFF implementation
The DFF gate logic implementation requires, among other things, connecting Nand gates with feedback loops
The resulting implementation is elegant, yet impossible to realize on the supplied hardware simulator
The hardware simulator does not allow loops of combinational chips (like Nand)
Therefore, we will use a built-in DFF implementation:
/** Data Flip-flop: out(t) = in(t-1)
* where t is the current time unit. */
CHIP DFF {
IN in;
OUT out;
BUILTIN DFF;
CLOCKED in;
}
Part of a possible DFF implementation

## Slide 96: Project 3
Given:
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
Build:
Bit
Register
PC
RAM8
RAM64
RAM512
RAM4K
RAM16K

## Slide 97: 1-bit Register
out
in
load
Bit
/** 1-bit register:
if load(t – 1) then out(t) = in(t – 1)
else out(t) = out(t – 1)) */
CHIP Bit {
IN in, load;
OUT out;
PARTS:
// Put your code here:
}
Bit.hdl
in
load
out
Implementation tip:
Follow the chip diagram

## Slide 98: 16-bit Register
Register.hdl
Register
in
16
out
16
load
/** 1-bit register:
if load(t – 1) then out(t) = in(t – 1)
else out(t) = out(t – 1)) */
CHIP Bit {
IN in[16], load;
OUT out[16];
PARTS:
// Put your code here:
}
16
out
load
16
in
...
Implementation tip:
Follow the chip diagram
Partial diagram, showing some of the chip-parts, without connections

## Slide 99: 16-bit Counter
Implementation tip: Can be built from a Register, an Incrementer, and Mux’s
/**
A 16-bit counter with control bits.
if reset(t – 1) out(t) = 0 // resetting
else if load(t – 1) out(t) = in(t – 1) // setting
else if inc(t – 1) out(t) = out(t – 1) + 1 // incrementing
else out(t) = out(t – 1) // maintaining
*/
CHIP PC {
IN in[16], load, inc, reset;
OUT out[16];
PARTS:
// Put your code here:
}
PC (counter)
in
16
out
16
load
inc
reset

## Slide 100: Project 3
Given
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
Build the following chips
Bit
Register
PC
RAM8
RAM64
RAM512
RAM4K
RAM16K

## Slide 101: 8-Register RAM: Abstraction
/*
Let M stand for the state of the register
selected by address.
if load(t – 1) then {M = in(t), out(t) = M}
else out(t) = M
*/
CHIP RAM8 {
IN in[16], load, address[3];
OUT out[16];
PARTS:
// Put your code here:
}
RAM8.hdl
out
in
load
Register
...
RAMn
Register
Register
address
3
16
16

## Slide 102: 8-Register RAM: Implementation
DMux
(1 to 8)
Register
in
16
load
out
Register
in
load
out
Register
in
load
out
...
Mux
(8 to 1)
out
16
in
16
address
3
load
Partial diagram, showing some of the chip-parts, without connections
Implementation tip:
Follow the chip diagram
16
16
16
16
16

## Slide 103: Project 3
Given
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
A family of RAM chips
Build the following chips
Bit
Register
PC
RAM8
RAM64
RAM512
RAM4K
RAM16K

## Slide 104: n-Register RAM
out
in
load
16
Register
...
RAMn
Register
Register
address
k
16
/*
Let M stand for the state of the register
selected by address.
if load(t – 1) then {M = in(t), out(t) = M}
else out(t) = M
*/
CHIP RAMn {
IN in[16], load, address[k];
OUT out[16];
PARTS:
// Put your code here:
}
RAMn.hdl
Notes: Albert Einstein about achieving maximum functionality with minimum rules.

## Slide 105: n-Register RAM
chip name | n | k
RAM8 | 8 | 3
RAM64 | 64 | 6
RAM512 | 512 | 9
RAM4K | 4096 | 12
RAM16K | 16384 | 14
out
in
load
16
Register
...
RAMn
Register
Register
address
k
16
Implementation tips
Think about the RAM’s address input as consisting of two fields:
  One field selects a RAM-part;
  The other field selects a register within that RAM-part
Use logic gates to effect this addressing scheme.
Notes: Albert Einstein about achieving maximum functionality with minimum rules.

## Slide 106: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 107: Project 3
www.nand2tetris.org
All the necessary project 3 files are available in:
nand2tetris / projects / 03

## Slide 108: Resources
Project 3 folder (.hdl, .tst, .cmp files): nand2tetris/projects/03
Tools
  Text editor (for completing the given .hdl stub-files)
  Hardware simulator: nand2tetris/tools
Guides
  Hardware Simulator Tutorial
  HDL Guide
  Hack Chip Set API

## Slide 109: Best practice advice
Implement the chips in the order in which they appear in the project guidelines
If you don’t implement some chips, you can still use their built-in implementations
No need for “helper chips”: Implement / use only the chips we specified
In each chip definition, strive to use as few chip-parts as possible
You will have to use chips implemented in previous projects;
For efficiency and consistency’s sake, use their built-in versions, rather than your own HDL implementations.
That’s It!
Go Do Project 3!
For technical reasons, the chips of project 3 are organized in two sub-folders named projects/03/a and projects/03/b
When writing and simulating the .hdl files, leave this folder structure as is.

## Slide 110: Chapter 3: Memory
  Implementation
  Data Flip Flop
  Registers
  RAM
  Project 3: Chips
  Project 3: Guidelines
  Abstraction
  Representing time
  Clock
  Registers
  RAM
  Counters

## Slide 111: What’s next?
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p2
p3
p4
p5
p6
This lecture / chapter / project:
Build the computer’s RAM

## Slide 112: What’s next?
hardware platform
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
Building chips
Building a computer
abstraction
assembler
machine language
p1
p2
p3
p4
p5
p6
Next lecture / chapter / project:
Get acquainted with the computer architecture
Write machine language programs