## Slide 1
Chapter 4
Machine Language
From Nand to Tetris
Building a Modern Computer from First Principles
These slides support chapter 4 of the book
The Elements of Computing Systems
(1st and 2nd editions)
By Noam Nisan and Shimon Schocken
MIT Press

## Slide 2: Usage Notice
  You are welcome to use this presentation, or any part of it, in Nand to Tetris courses, or in other courses, as you see fit.
  Usage is free provided that it supports instruction in educational, non-profit settings.
  You can use the slides as-is, or modify them as needed.
  We’ll appreciate it if you will credit Nand to Tetris somewhere, and put a reference to www.nand2tetris.org
  Happy teaching!
  Shimon Schocken / Noam Nisan

## Slide 3: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
In previous chapters we’ve built the computer’s ALU and RAM

## Slide 4: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
p4
Writing low-level programs
In this chapter we’ll become familiar with:
The Hack computer / instruction set
Low-level programming
Assembly / assemblers
In previous chapters we’ve built the computer’s ALU and RAM

## Slide 5: Computers are flexible and versatile
Same hardware can run many different programs (software)

## Slide 6: Computers are flexible and versatile
Ada Lovelace
(1843)
Early symbolic program
Landmark “proof of concept” that computers can be programmed
Same hardware can run many different programs (software)

## Slide 7: Computers are flexible and versatile
Alan Turing
(1936)
Universal Turing Machine
Landmark article, describing a theoretical general-purpose computer
Same hardware can run many different programs (software)

## Slide 8: Computers are flexible and versatile
First general-purpose computer
Eniac, University of Pennsylvania, 1945
Same hardware can run many different programs (software)

## Slide 9: Computer architecture
ALU
Memory
CPU
registers
output
input

## Slide 10: Computer architecture
ALU
program
Memory
CPU
registers
output
input
data

## Slide 11: Computer architecture
ALU
Memory
CPU
registers
0
1
2
...
1100101010010101
1100100101100111
0011001010101011
...
instructions
data
output
input
0101110011100110
1100000010010001
1110001011111100
...

## Slide 12: Computer architecture
ALU
Memory
CPU
registers
0
1
2
...
1100101010010101
1100100101100111
0011001010101011
...
instructions
data
output
input
0101110011100110
1100000010010001
1110001011111100
...
instruction

## Slide 13: Computer architecture
ALU
Memory
CPU
registers
0
1
2
...
1100101010010101
1100100101100111
0011001010101011
...
instructions
data
output
input
0101110011100110
1100000010010001
1110001011111100
...
instruction
Data value
Stored program concept
The computer memory can store programs, just like it stores data
Programs = data.
One of the most important ideas in the history of computer science

## Slide 14: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 15: Machine Language
CPU
ALU
10
5
137



Registers
R1
R2
A
Memory
12
615
8828
0
1
2
3
3
-5
...
955
20
136
137
-523
138
...
Computer
(Conceptual definition):
A processor (CPU) that manipulates a set of registers:
CPU-resident registers (few, accessed directly, by name)
Memory-resident registers (many, accessed by supplying an address)
Machine language
A formalism specifying how to access and manipulate registers.

## Slide 16: Registers
Data registers:
Hold data values
Address register:
Holds an address
Instruction register:
Holds an instruction
All these registers are… registers (containers that hold bits)
The number and bit-width of the registers vary greatly from one computer to another.
CPU
ALU
10
5
137



Registers
R1
R2
A
Memory
12
615
8828
0
1
2
3
3
-5
...
955
20
136
137
-523
138
...

## Slide 17: Typical operations
// R1  73
load R1, 73
// R1  R1 + R2
add R1, R2
CPU
ALU
10
5
137



Registers
R1
R2
A
Memory
12
615
8828
0
1
2
3
3
-5
...
955
20
136
137
-523
138
...

## Slide 18: Typical operations
// R1  73
load R1, 73
// R1  R1 + R2
add R1, R2
// R1  R1 + Memory[137]
add R1, M[137]
// R1  Memory[A]
load R1, @A
CPU
ALU
10
5
137



Registers
R1
R2
A
Memory
12
615
8828
0
1
2
3
3
-5
...
955
20
136
137
-523
138
...
The syntax of machine languages varies greatly from one computer to another, but all of them are designed to do the same thing: Manipulate registers.

## Slide 19: Control
CPU
ALU
000000000010010
0000000000000101
00000010110000



Registers
R1
R2
A
Memory
1110111100001010
1100000011111110
0110111100001010
0
1
2
1100000011111110
3
0101100011100110
...
0001100011011100
1100000011111110
136
137
0101110010001110
138
...

## Slide 20: Control
CPU
ALU
000000000010010
0000000000000101
00000010110000



Registers
R1
R2
A
Memory
1110111100001010
1100000011111110
0110111100001010
0
1
2
1100000011111110
3
0101100011100110
...
0001100011011100
1100000011111110
136
137
0101110010001110
138
...
current instruction
Which instruction should be executed next?
By default, the CPU executes the next instruction
Sometimes we want to “jump” to execute another instruction

## Slide 21: Control
Unconditional branching
Execute some instruction other than the next one
Example: Embarking on a new iteration in a loop
...
// Adds 1 to R1, repetitively
Basic version

## Slide 22: Control
Unconditional branching
Execute some instruction other than the next one
Example: Embarking on a new iteration in a loop
...
// Adds 1 to R1, repetitively
(LOOP)
add R1,1
...
goto LOOP
...
Symbolic version
...
// Adds 1 to R1, repetitively
add R1,1
...
goto 13
...
Basic version
13
...
27
...
Programs with symbolic references are …
Easier to develop
Readable
Relocatable.
Line numbers
Physical addresses
No line numbers
Symbolic addresses

## Slide 23: Control
Conditional branching
Sometimes we want to “jump” to execute another instruction, but only if a certain condition is met
// Set R1 to abs(R1).
Symbolic program

## Slide 24: Control
Conditional branching
Sometimes we want to “jump” to execute another instruction, but only if a certain condition is met
Symbolic program
// Set R1 to abs(R1).
// if R1 > 0 goto CONT
jgt R1,CONT
CONT:
// Here R1 is non-negative
...
conditional goto

## Slide 25: Control
Conditional branching
Sometimes we want to “jump” to execute another instruction, but only if a certain condition is met
// Set R1 to abs(R1).
// if R1 > 0 goto CONT
jgt R1,CONT
// R1 ← –R1
store R2,R1
store R1,0
subt R1,R2
CONT:
// Here R1 is non-negative
...
Symbolic program
How can we actually execute the program?

## Slide 26: Control
Conditional branching
Sometimes we want to “jump” to execute another instruction, but only if a certain condition is met
// Set R1 to abs(R1).
// if R1 > 0 goto CONT
jgt R1,CONT
// R1 ← –R1
store R2,R1
store R1,0
subt R1,R2
CONT:
// Here R1 is non-negative
...
Symbolic program
0101111100111100
1010101010101010
1100000010101010
1011000010000001
...
Binary code
translate
load and execute
Assembler
Assembly

## Slide 27: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 28: The Hack computer
Hack is a 16-bit computer, featuring two memory units
The address input of each memory unit is 15-bit wide
Question: How many words can each memory unit have?
Answer: The address space of each memory unit is 215 = 32K words.
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
0
1
2
...
D
0010101010110110
1111100100101011
0011101001011011
1110011001011001
0000110011100111
1000110000110000
0000010011111100
0
1
2
...
0000011100110010
1001000011110101
0001101001101111
(Conceptual, partial view of the Hack computer architecture)

## Slide 29: Memory
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
0
1
2
...
D
0010101010110110
1111100100101011
0011101001011011
1110011001011001
0000110011100111
1000110000110000
0000010011111100
0
1
2
...
0000011100110010
1001000011110101
0001101001101111
...
32766
32767
...
32766
32767
RAM
Read-write data memory
Addressed by the A register
(Conceptual, partial view of the Hack computer architecture)

## Slide 30: Memory
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
...
32766
32767
...
32766
32767
0
1
2
...
D
0010101010110110
1111100100101011
0011101001011011
1110011001011001
0000110011100111
1000110000110000
0000010011111100
0
1
2
...
0000111100110010
0000011100110010
1001000011110101
0001101001101111
M
RAM
Read-write data memory
Addressed by the A register
The selected register, RAM[A], is represented by the symbol M
(Conceptual, partial view of the Hack computer architecture)

## Slide 31: Memory
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
...
32766
32767
...
32766
32767
0
1
2
...
D
0010101010110110
1111100100101011
0011101001011011
1110011001011001
0000110011100111
1000110000110000
0000010011111100
0
1
2
...
0000111100110010
0000011100110010
1001000011110101
0001101001101111
M
Loaded with a sequence of 16-bit Hack instructions
RAM
Read-write data memory
Addressed by the A register
The selected register, RAM[A], is represented by the symbol M
ROM
Read-only instruction memory
(Conceptual, partial view of the Hack computer architecture)

## Slide 32: Memory
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
...
32766
32767
...
32766
32767
0
1
2
...
1001111100011001
D
0010101010110110
1111100100101011
0011101001011011
1110011001011001
0000110011100111
1000110000110000
0000010011111100
0
1
2
...
0000111100110010
0000011100110010
1001000011110101
0001101001101111
M
Loaded with a sequence of 16-bit Hack instructions
RAM
Read-write data memory
Addressed by the A register
The selected register, RAM[A], is represented by the symbol M
ROM
Read-only instruction memory
Addressed by the (same) A register
The selected register, ROM[A], contains the “current instruction”
(Conceptual, partial view of the Hack computer architecture)

## Slide 33: Memory
ROM
Read-only instruction memory
Addressed by the (same) A register
The selected register, ROM[A], contains the “current instruction”
RAM
Read-write data memory
Addressed by the A register
The selected register, RAM[A], is represented by the symbol M
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
...
32766
32767
...
32766
32767
0
1
2
...
1001111100011001
D
0010101010110110
1111100100101011
0011101001011011
1110011001011001
0000110011100111
1000110000110000
0000010011111100
0
1
2
...
0000111100110010
0000011100110010
1001000011110101
0001101001101111
M
Loaded with a sequence of 16-bit Hack instructions
Should we focus on RAM[A], or on ROM[A]?
Depends on the current instruction (later)
(Conceptual, partial view of the Hack computer architecture)

## Slide 34: Registers
D: data register
A: address register
M: the selected RAM register
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
...
32766
32767
...
32766
32767
0
1
2
...
0
1
2
...
M
instruction
D
(Conceptual, partial view of the Hack computer architecture)

## Slide 35: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 36: Hack instructions
A instruction
C instruction
  Instruction set

## Slide 37: Hack instructions
A instruction
C instruction
  Instruction set
Side effects:
RAM[A] (called M) becomes selected
ROM[A] becomes selected
Syntax:
where const is a constant
@ const
Example:
@ 19
Semantics:
A ← 19
(Complete / formal syntax, later).

## Slide 38: Hack instructions
D=0
A=–1
M=1
...
Examples:
Syntax:
reg = {0 | 1 | –1}
where reg = {A | D | M}
reg1 = reg2
where reg1 = {A | D | M}
reg2 = [–] {A | D | M}
D=A
D=M
M=–M
...
where reg, reg1 = {A | D | M}, op = {+ | –}, and
reg2 = {A | D | M | 1} and reg1 reg2
reg = reg1 op reg2
D=D+M
A=A–1
M=D+1
...
(Complete / formal syntax, later).
A instruction
C instruction
  Instruction set

## Slide 39: Hack instructions
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...
// D ← 2
Examples:
The game: We show some typical Hack instructions (top left), and practice writing code examples that use subsets of these instructions.
?

## Slide 40: Hack instructions
Examples:
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...
// D ← 2
D=1
D=D+1
// D ← 1954
Use only the instructions shown in this slide
?

## Slide 41: Hack instructions
// D ← 1954
@1954
D=A
// D ← 2
D=1
D=D+1
Examples:
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...
// D ← D + 23
Use only the instructions shown in thus slide
?

## Slide 42: Hack instructions
// D ← 1954
@1954
D=A
Observation
In these examples we use the address register A as a data register:
The addressing side-effects of A are ignored.
// D ← 2
D=1
D=D+1
// D ← D + 23
@23
D=D+A
Examples:
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 43: Hack instructions
// RAM[100] ← 0
More examples:
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 44: Hack instructions
// RAM[100] ← 0
@100
M=0
More examples:
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...
// RAM[100] ← 17

## Slide 45: Hack instructions
// RAM[100] ← 0
@100
M=0
// RAM[100] ← 17
@17
D=A
@100
M=D
First pair of instructions: A is used as a data register
Second pair of instructions: A is used as an address register
More examples:
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 46: Hack instructions
// RAM[100] ← 0
@100
M=0
// RAM[100] ← 17
@17
D=A
@100
M=D
More examples:
// RAM[100] ← RAM[200]
?
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 47: Hack instructions
// RAM[100] ← 0
@100
M=0
// RAM[100] ← 17
@17
D=A
@100
M=D
// RAM[100] ← RAM[200]
@200
D=M
@100
M=D
When we want to operate on a memory register, we typically need a pair of instructions:
A instruction: Selects a memory register
C instruction: Operates on the selected register.
More examples:
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 48: Hack instructions
// RAM[3] ← RAM[3] – 15
?
Use only the instructions shown in the current slide
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 49: Hack instructions
// RAM[3] ← RAM[3] – 15
@15
D=A
@3
M=M–D
// RAM[3] ← RAM[4] + 1
?
Use only the instructions shown in the current slide
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 50: Hack instructions
// RAM[3] ← RAM[3] – 15
@15
D=A
@3
M=M–D
// RAM[3] ← RAM[4] + 1
@4
D=M+1
@3
M=D
Use only the instructions shown in the current slide
Typical instructions:
@ constant
(A ← constant)
D=1
D=A
D=D+1
...
D=D+A
D=M
M=0
...
M=D
D=D+A
M=M–D
...

## Slide 51: Hack instructions
Typical instructions:
A=1
D=–1
M=0
...
A=M
D=M
M=D
...
A=D-A
D=D+A
D=D+M
...
@ constant
(A ← constant)
// Computes: RAM[2] = RAM[0] + RAM[1] + 17
Add.asm
?
Use only the instructions shown in the current slide

## Slide 52: Hack instructions
// Computes: RAM[2] = RAM[0] + RAM[1] + 17
// D = RAM[0]
@0
D=M
// D = D + RAM[1]
@1
D=D+M
// D = D + 17
@17
D=D+A
// RAM[2] = D
@2
M=D
Add.asm
Typical instructions:
A=1
D=–1
M=0
...
A=M
D=M
M=D
...
A=D-A
D=D+A
D=D+M
...
@ constant
(A ← constant)

## Slide 53: Hack instructions
// Computes: RAM[2] = RAM[0] + RAM[1] + 17
// D = RAM[0]
@0
D=M
// D = D + RAM[1]
@1
D=D+M
// D = D + 17
@17
D=D+A
// RAM[2] = D
@2
M=D
Add.asm
How can we tell that a given program actually works?
Testing / simulating
Formal verification
@ constant
(A ← constant)
Typical instructions:
A=1
D=–1
M=0
...
A=M
D=M
M=D
...
A=D-A
D=D+A
D=D+M
...
@ constant
(A ← constant)

## Slide 54: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 55: The CPU emulator
The CPU emulator is a Java program, designed to emulate the Hack CPU
On your PC (nand2tetris/tools)
code
execute

## Slide 56: The CPU emulator
// Computes: RAM[2] = RAM[0] + RAM[1] + 17
// D = RAM[0]
@0
D=M
// D = D + RAM[1]
@1
D=D+M
// D = D + 17
@17
D=D+A
// RAM[2] = D
@2
M=D
Add.asm (example)
When loading a symbolic program into the CPU emulator, the emulator translates it into binary code (using a built-in assembler)
Execute
Load into the CPU emulator
0000000000000000
1000010010001101
0000000000000001
1010011001100001
0000000000010001
1001111100110011
0000000000000010
1110010010010011
Binary

## Slide 57: The CPU emulator
CPU emulator
demo

## Slide 58: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 59: Loading a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
M
ROM
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
Hack program
load

## Slide 60: Loading a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
M
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
Hack program
load
Convention:
The first instruction is loaded into address 0, the next instruction into address 1, and so on.

## Slide 61: Executing a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
M

## Slide 62: Executing a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
M

## Slide 63: Executing a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
M

## Slide 64: Executing a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
M

## Slide 65: Executing a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
M

## Slide 66: Executing a program
Instruction memory
RAM
Data memory
Address register
Data register
A
0
1
2
...
0
1
2
...
D
instruction
instruction
instruction
instruction
instruction
instruction
instruction
instruction
M
The default: Execute the next instruction
Suppose we wish to execute another instruction
How to specify this branching?

## Slide 67: Branching
Flow of control:
0,1,2,3,4,
7,8,9,
2,3,4,
7,8,9,
2,3,4,
...
instruction
instruction
instruction
instruction
goto 7
instruction
instruction
instruction
instruction
goto 2
instruction
...
0
1
2
3
4
5
6
7
8
9
10
11
Unconditional branching example (pseudocode)

## Slide 68: Branching
Flow of control:
0,1,2,3,4,
if condition is true
7,8,9,...
else
5,6,7,8,9,...
instruction
instruction
instruction
instruction
if (condition) goto 7
instruction
instruction
instruction
instruction
instruction
...
0
1
2
3
4
5
6
7
8
9
...
Conditional branching
example (pseudocode)

## Slide 69: Branching
Example (Pseudocode):
instruction
instruction
goto 6
instruction
instruction
instruction
instruction
instruction
...
0
1
2
3
4
5
6
7
...
…
// goto 6
@6
0;JMP
…
In Hack:
Branching in the Hack language:
Semantics of 0;JMP
Jump to the instruction stored in the register selected by A
(the “0;” prefix will be explained later)

## Slide 70: Branching
D;JGT // if D 0 jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Example (Pseudocode):
0
1
2
3
4
5
6
7
...
instruction
instruction
if (D > 0) goto 6
instruction
instruction
instruction
instruction
instruction
...
Branching in the Hack language:
In Hack:
…
// if (D > 0) goto 6
@6
D;JGT
…

## Slide 71: Branching
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
Typical branching instructions:
0
1
2
3
4
5
6
7
...
0
1
2
3
4
5
6
7
...
instruction
instruction
if (D > 0) goto 6
instruction
instruction
instruction
instruction
instruction
...
In Hack:
to the instruction stored in
ROM[A]
Branching in the Hack language:
Example (Pseudocode):
…
// if (D > 0) goto 6
@6
D;JGT
…

## Slide 72: Branching
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
0
1
2
3
4
5
6
7
...
instruction
instruction
if (D > 0) goto 6
instruction
instruction
instruction
instruction
instruction
...
In Hack:
to the instruction stored in
ROM[A]
Branching in the Hack language:
…
// if (D > 0) goto 6
@6
D;JGT
…
Example (Pseudocode):

## Slide 73: Branching
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Typical instructions:
A=1
D=-1
M=0
...
A=M
D=A
M=D
...
D=D-A
A=A-1
M=D+1
...
@ constant
(A ← constant)
// if )D = 0( goto 300
Use only the instructions shown in the current slide
?

## Slide 74: Branching
// if )D = 0( goto 300
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Typical instructions:
A=1
D=-1
M=0
...
A=M
D=A
M=D
...
D=D-A
A=A-1
M=D+1
...
@ constant
(A ← constant)
Use only the instructions shown in the current slide

## Slide 75: Branching
// if )D = 0( goto 300
@300
D;JEQ
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Typical instructions:
A=1
D=-1
M=0
...
A=M
D=A
M=D
...
D=D-A
A=A-1
M=D+1
...
@ constant
(A ← constant)
Use only the instructions shown in the current slide

## Slide 76: Branching
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Typical instructions:
A=1
D=-1
M=0
...
A=M
D=A
M=D
...
D=D-A
A=A-1
M=D+1
...
@ constant
(A ← constant)

## Slide 77: Branching
// if (RAM[3] < 100) goto 12
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Typical instructions:
A=1
D=-1
M=0
...
A=M
D=A
M=D
...
D=D-A
A=A-1
M=D+1
...
@ constant
(A ← constant)
Use only the instructions shown in the current slide
?

## Slide 78: Branching
// if (RAM[3] < 100) goto 12
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Typical instructions:
A=1
D=-1
M=0
...
A=M
D=A
M=D
...
D=D-A
A=A-1
M=D+1
...
@ constant
(A ← constant)
Use only the instructions shown in the current slide

## Slide 79: Branching
// if (RAM[3] < 100) goto 12
// D = RAM[3] – 100
@3
D=M
@100
D=D–A
// if (D < 0) goto 12
@12
D;JLT
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
Typical branching instructions:
to the instruction stored in
ROM[A]
Typical instructions:
A=1
D=-1
M=0
...
A=M
D=A
M=D
...
D=D-A
A=A-1
M=D+1
...
@ constant
(A ← constant)
Use only the instructions shown in the current slide

## Slide 80: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 81: Hack instructions
A instruction
C instruction
Syntax:
where const is a constant
@ const
Example:
@ 19 // A ← 19
For example, if x is bound to 21, this instruction will set A to 21
@ sym
where sym is a symbol bound to a constant
@ x
This idiom can be used for realizing:
Variables
Labels

## Slide 82: Variables
...
i = 1
sum = 0
...
sum = sum + i
i = i + 1
...
Pseudocode (example)
...
// i = 1
Hack assembly
write

## Slide 83: Variables
...
i = 1
sum = 0
...
sum = sum + i
i = i + 1
...
Pseudocode (example)
...
// i = 1
@i
M=1
// sum = 0
@sum
M=0
...
// sum = sum + i
@i
D=M
@sum
M=D+M
// i = i + 1
@i
M=M+1
...
Hack assembly
Symbolic programming
The code writer is allowed to use symbolic variables, as needed
We assume that there is an agent who knows how to bind these symbols to selected RAM addresses
This agent is the assembler
For example
If the assembler will bind i to 16 and sum to 17, every instruction @i and @sum will end up selecting RAM[16] and RAM[17]
Should the code writer worry about what is the actual bindings? No
The result: a low-level model for representing variables.
write

## Slide 84: Variables
Use only the instructions shown in the current slide
// sum = 0
?
// x = 512
?
// n = n – 1
?
// sum = sum + x
?
A ← the constant which is bound to symbol
Typical instructions:
@ symbol
@ constant
A ← constant
D=0
M=1
D=–1
M=0
...
D=M
A=M
M=D
D=A
...
D=D+A
D=A+1
D=D+M
M=M–1
...

## Slide 85: Variables
// sum = sum + x
@sum
D=M
@x
D=D+M
@sum
M=D
// sum = 0
@sum
M=0
// n = n – 1
@n
M=M–1
// x = 512
@512
D=A
@x
M=D
Use only the instructions shown in the current slide
A ← the constant which is bound to symbol
Typical instructions:
@ symbol
@ constant
A ← constant
D=0
M=1
D=–1
M=0
...
D=M
A=M
M=D
D=A
...
D=D+A
D=A+1
D=D+M
M=M–1
...

## Slide 86: Variables
Example:
// Sets R1 to 2 * R0
// Usage: Enter a value in R0
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
As if you have 16 built-in variables named R0…R15
We sometimes call them “virtual registers”
0
R0
1
R1
2
R2
...
...
15
R15
16
17
...
32767
RAM
Pre-defined symbols

## Slide 87: Variables
Example:
// Sets R1 to 2 * R0
// Usage: Enter a value in R0
@R0
D=M
@R1
M=D
M=D+M
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
As if you have 16 built-in variables named R0…R15
We sometimes call them “virtual registers”
0
R0
1
R1
2
R2
...
...
15
R15
16
17
...
32767
RAM
Pre-defined symbols
The use of R0, R1, … (instead of physical addresses 0, 1, …) makes it easier to document, write, and debug Hack code.

## Slide 88: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 89: Labels
Typical branching instructions:
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
to
ROM[A]
// if (RAM[100] < 0) goto 35
// goto 48
// if (D > 0) goto 21
Examples (similar to what we did before):
?
?
?

## Slide 90: Labels
// if (RAM[100] < 0) goto 35
@100
D=M
@35
D;JLT
// goto 48
@48
0;JMP
Typical branching instructions:
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
to
ROM[A]
// if (D > 0) goto 21
@21
D;JGT
// if (x < 0) goto NEG
// goto LOOP
// if (D > 0) goto CONT
Examples (similar to what we did before):
Same examples, using labels

## Slide 91: Labels
// if (RAM[100] < 0) goto 35
@100
D=M
@35
D;JLT
// goto 48
@48
0;JMP
Typical branching instructions:
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
to
ROM[A]
// if (D > 0) goto 21
@21
D;JGT
// if (x < 0) goto NEG
// goto LOOP
@LOOP
0;JMP
// if (D > 0) goto CONT
Examples (similar to what we did before):
Same examples, using labels

## Slide 92: Labels
// if (RAM[100] < 0) goto 35
@100
D=M
@35
D;JLT
// goto 48
@48
0;JMP
Typical branching instructions:
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
to
ROM[A]
// if (D > 0) goto 21
@21
D;JGT
// if (x < 0) goto NEG
// goto LOOP
@LOOP
0;JMP
// if (D > 0) goto CONT
@CONT
D;JGT
Examples (similar to what we did before):
Same examples, using labels

## Slide 93: Labels
// if (RAM[100] < 0) goto 35
@100
D=M
@35
D;JLT
// goto 48
@48
0;JMP
Typical branching instructions:
D;JGT // if D 0 jump
D;JGE // if D 0 jump
D;JLT // if D 0 jump
D;JLE // if D 0 jump
D;JEQ // if D 0 jump
D;JNE // if D 0 jump
0;JMP // jump
to
ROM[A]
// if (D > 0) goto 21
@21
D;JGT
// if (x < 0) goto NEG
@x
D=M
@NEG
D;JLT
// goto LOOP
@LOOP
0;JMP
// if (D > 0) goto CONT
@CONT
D;JGT
Examples (similar to what we did before):
Same examples, using labels
Hack convention:
Variables: lower-case symbols
Labels: upper-case symbols

## Slide 94: Labels
...
LOOP:
if (i = 0) goto CONT
do this
...
goto LOOP
CONT:
do that
...
Hack assembly
write
Example (pseudocode)

## Slide 95: Labels
Example (pseudocode)
...
LOOP:
if (i = 0) goto CONT
do this
...
goto LOOP
CONT:
do that
...
Hack assembly
...
(LOOP)
// if (i = 0) goto CONT
@i
D=M
@CONT
D;JEQ
do this
...
// goto LOOP
@LOOP
0;JMP
(CONT)
do that
...
Hack assembly syntax:
A label sym is declared using (sym)
Any label sym declared somewhere in the program can appear in a @sym instruction
The assembler resolves the labels to actual addresses.
Programs that use symbolic labels and variables are...
Easy to write / translate from pseudocode
Readable
Relocatable.
write

## Slide 96: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 97: Program example 1: Add
// Sets R2 to R0 + R1 + 17
Add.asm
Task: R2 ← R0 + R1 + 17

## Slide 98: Program example 1: Add
// Sets R2 to R0 + R1 + 17
// D = R0
@R0
D=M
// D = D + R1
@R1
D=D+M
// D = D + 17
@17
D=D+A
// R2 = D
@R2
M=D
Add.asm
Task: R2 ← R0 + R1 + 17

## Slide 99: Program example 2: Signum
// if R0 >= 0 then R1 = 1
// else R1 = –1
Pseudocode

## Slide 100: Program example 2: Signum
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
Signum.asm
write

## Slide 101: Program example 2: Signum
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
Best practice
When writing a (non-trivial) assembly program, always start with writing pseudocode.
Then translate the pseudo instructions into assembly, line by line.
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
write

## Slide 102: Program example 2: Signum
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
@0
0
Memory
D=M
1
@8
2
D;JGE
3
@1
4
M=–1
5
@10
6
0;JMP
7
@1
8
M=1
9
10
11
12
13
14
...
Assembler / loader
(Note how the assembler mapped all the symbols on physical addresses)

## Slide 103: Watch out: Security breach
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
@0
0
Memory
D=M
1
@8
2
D;JGE
3
@1
4
M=–1
5
@10
6
0;JMP
7
@1
8
M=1
9
10
11
12
13
14
...
Assembler / loader

## Slide 104: Watch out: Security breach
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
0111111000111110
1010101001011110
0101011100110111
@0
0
Memory
D=M
1
@8
2
D;JGE
3
@1
4
M=–1
5
@10
6
0;JMP
7
@1
8
M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Assembler / loader
The memory is never empty

## Slide 105: Watch out: Security breach
0111111000111110
1010101001011110
0101011100110111
@0
0
Memory
D=M
1
@8
2
D;JGE
3
@1
4
M=–1
5
@10
6
0;JMP
7
@1
8
M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)

## Slide 106: Watch out: Security breach
Program execution:
0111111000111110
1010101001011110
0101011100110111
@0
0
Memory
D=M
1
@8
2
D;JGE
3
@1
4
M=–1
5
@10
6
0;JMP
7
@1
8
M=1
9
10
11
12
13
14
...
Malicious
Code
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)

## Slide 107: Watch out: Security breach
Program execution:
0111111000111110
1010101001011110
0101011100110111
@0
0
Memory
D=M
1
@8
2
D;JGE
3
@1
4
M=–1
5
@10
6
0;JMP
7
@1
8
M=1
9
10
11
12
13
14
...
Malicious
Code
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)

## Slide 108: Terminating programs properly
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode

## Slide 109: Terminating programs properly
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP
Infinite loop

## Slide 110: Terminating programs properly
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=-1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
Assembler / loader
Infinite loop

## Slide 111: Terminating programs properly
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 112: Terminating programs properly
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 113: Terminating programs properly
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 114: Terminating programs properly
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 115: Terminating programs properly
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 116: Terminating programs properly
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 117: Terminating programs properly
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
Program execution:
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 118: Terminating programs properly
Best practice:
Terminate every assembly program with an infinite loop.
@10
0;JMP
0101011100110111
@0
0
Memory
@D=M
1
@8
2
@D;JGE
3
@1
4
@M=–1
5
@10
6
@0;JMP
7
@1
8
@M=1
9
10
11
12
13
14
...
0100100110011011
1110010011111111
// if R0 >= 0 then R1 = 1
// else R1 = –1
if (R0 0) goto POS
R1 = –1
goto END
POS:
R1 = 1
END:
Signum.asm
Pseudocode
// if R0 >= 0 then R1 = 1
// else R1 = –1
// if R0 >= 0 goto POS
@R0
D=M
@POS
D;JGE
// R1 = –1
@R1
M=–1
// goto END
@END
0;JMP
(POS)
// R1 = 1
@R1
M=1
(END)
@END
0;JMP

## Slide 119: Program example 3: Max
Task: Set R0 to max(R1, R2)
Examples: max(5,3) = 5, max(2,7) = 7, max(4,4) = 4
// if (R1 > R2) then R0 = R1
// else R0 = R2
...
Pseudocode

## Slide 120: Program example 3: Max
Task: Set R0 to max(R1, R2)
Examples: max(5,3) = 5, max(2,7) = 7, max(4,4) = 4
// if (R1 > R2) then R0 = R1
// else R0 = R2
...
Pseudocode
// You do it
Max2.asm
Write the pseudocode
Translate and write the assembly code in a text file named Max2.asm
Load Max2.asm into the CPU emulator
Put some values in R1 and R2
Run the program, one instruction at a time
Make sure that the program puts the correct value in R0.
write

## Slide 121: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 122: Iterative processing
Example: Compute 1 + 2 + 3 + ... + N
Pseudocode
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0

## Slide 123: Iterative processing
Pseudocode
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
i = 1
sum = 0
LOOP:
if (i > R0) goto STOP
sum = sum + i
i = i + 1
goto LOOP
STOP:
R1 = sum
Example: Compute 1 + 2 + 3 + ... + N

## Slide 124: Iterative processing
Pseudocode
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
i = 1
sum = 0
LOOP:
if (i > R0) goto STOP
sum = sum + i
i = i + 1
goto LOOP
STOP:
R1 = sum
Hack assembly
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
Example: Compute 1 + 2 + 3 + ... + N

## Slide 125: Iterative processing
Pseudocode
Hack assembly
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if (i > R0) goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum = sum + i
@sum
D=M
@i
D=D+M
@sum
M=D
// i = i + 1
@i
M=M+1
// goto LOOP
@LOOP
0;JMP
(code continues here)
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
i = 1
sum = 0
LOOP:
if (i > R0) goto STOP
sum = sum + i
i = i + 1
goto LOOP
STOP:
R1 = sum
Example: Compute 1 + 2 + 3 + ... + N

## Slide 126: Iterative processing
Pseudocode
Hack assembly
(code continues here)
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if (i > R0) goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum = sum + i
@sum
D=M
@i
D=D+M
@sum
M=D
// i = i + 1
@i
M=M+1
// goto LOOP
@LOOP
0;JMP
(STOP)
// R1 = sum
@sum
D=M
@R1
M=D
// infinite loop
(END)
@END
0;JMP
Example: Compute 1 + 2 + 3 + ... + N
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
i = 1
sum = 0
LOOP:
if (i > R0) goto STOP
sum = sum + i
i = i + 1
goto LOOP
STOP:
R1 = sum

## Slide 127: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 128: Pointer-based processing
Example 1: Set the register at address addr to –1
Input: R0: Holds addr
0
R0
1
R1
2
R2
...
...
15
16
17
...
255
256
...
1012
1013
1014
1015
RAM
1016
...
// Sets RAM[R0] to –1
// Usage: Put some non-negative value in R0

## Slide 129: Pointer-based processing
// Sets RAM[R0] to –1
// Usage: Put some non-negative value in R0
1013
0
R0
1
R1
2
R2
...
...
15
16
17
...
255
256
...
1012
-1
1013
1014
1015
RAM
desired result
1016
...
Example 1: Set the register at address addr to –1
Input: R0: Holds addr

## Slide 130: Pointer-based processing
// Sets RAM[R0] to –1
// Usage: Put some non-negative value in R0
@R0
A=M
M=-1
The key instruction:
In the Hack machine language, pointer-based processing is realized by setting the address register to the address that we want to access, using the instruction A = …
1013
0
R0
1
R1
2
R2
...
...
15
16
17
...
255
256
...
1012
-1
1013
1014
1015
RAM
desired result
1016
...
Example 1: Set the register at address addr to –1
Input: R0: Holds addr

## Slide 131: Pointer-based processing
// Sets RAM[R0] to –1
// Usage: Put some non-negative value in R0
@R0
A=M
M=-1
0
R0
1
R1
2
R2
...
...
15
16
17
...
255
256
...
1012
1013
1014
1015
RAM
1016
...
// Sets RAM[R0] to R1
// Usage: Put some non-negative value in R0,
// and some value in R1.
Example 2:
Example 1: Set the register at address addr to –1
Input: R0: Holds addr

## Slide 132: Pointer-based processing
// Sets RAM[R0] to –1
// Usage: Put some non-negative value in R0
@R0
A=M
M=-1
1015
0
R0
-17
1
R1
2
R2
...
...
15
16
17
...
255
256
...
1012
1013
1014
-17
1015
RAM
desired result
1016
...
// Sets RAM[R0] to R1
// Usage: Put some non-negative value in R0,
// and some value in R1.
?
Example 2:
Example 1: Set the register at address addr to –1
Input: R0: Holds addr

## Slide 133: Pointer-based processing
// Sets RAM[R0] to –1
// Usage: Put some non-negative value in R0
@R0
A=M
M=-1
// Sets RAM[R0] to R1
// Usage: Put some non-negative value in R0,
// and some value in R1.
@R1
D=M
@R0
A=M
M=D
1015
0
R0
-17
1
R1
2
R2
...
...
15
16
17
...
255
256
...
1012
1013
1014
-17
1015
RAM
desired result
1016
...
Example 2:
Example 1: Set the register at address addr to –1
Input: R0: Holds addr

## Slide 134: Pointer-based processing
// Gets R1 = RAM[R0]
// Usage: Put some non-negative value in R0
Example 3: Get the value of the register at addr
Input: R0: Holds addr
0
R0
1
R1
2
R2
...
...
15
16
17
...
255
256
...
1012
1013
1014
1015
RAM
1016
...

## Slide 135: Pointer-based processing
// Gets R1 = RAM[R0]
// Usage: Put some non-negative value in R0
1013
0
R0
75
1
R1
2
R2
...
...
15
16
17
...
255
256
...
512
1012
75
1013
19
1014
-17
256
1015
RAM
desired result
1016
...
?
Example 3: Get the value of the register at addr
Input: R0: Holds addr

## Slide 136: Pointer-based processing
1013
0
R0
75
1
R1
2
R2
...
...
15
16
17
...
255
256
...
512
1012
75
1013
19
1014
-17
256
1015
RAM
desired result
1016
...
// Gets R1 = RAM[R0]
// Usage: Put some non-negative value in R0
@R0
A=M
D=M
@R1
M=D
Example 3: Get the value of the register at addr
Input: R0: Holds addr

## Slide 137: Pointer-based processing
0
R0
1
R1
2
R2
...
...
15
R15
16
17
...
255
256
...
300
301
302
303
304
305
...
RAM
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n

## Slide 138: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
16
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
base
n

## Slide 139: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
16
17
...
255
256
...
300
301
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 140: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
0
16
i
17
...
255
256
...
300
301
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 141: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
0
16
i
17
...
255
256
...
–1
300
301
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 142: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
1
16
i
17
...
255
256
...
–1
300
301
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 143: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
1
16
i
17
...
255
256
...
–1
300
–1
301
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 144: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
2
16
i
17
...
255
256
...
–1
300
–1
301
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 145: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
2
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 146: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
3
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 147: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
3
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 148: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
4
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 149: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
4
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 150: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
5
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 151: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
5
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 152: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
5
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
...
// RAM[R0 + i] = –1
?
The key operation
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 153: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
5
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
...
// RAM[R0 + i] = –1
@R0
D=M
@i
A=D+M
M=-1
...
The key operation
Example 4: Set the first n entries of the memory block beginning in address base to –1
Inputs: R0: base R1: n
Example: base = 300, n = 5
base
n

## Slide 154: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
Pseudocode
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1

## Slide 155: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
Pseudocode
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
i = 0
LOOP:
if (i == R1) goto END
RAM[R0 + i] = -1
i = i + 1
goto LOOP
END:

## Slide 156: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
16
i
17
...
255
256
...
-1
300
-1
301
-1
302
-1
303
-1
304
305
...
RAM
desired output
Assembly code
Pseudocode
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
?
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
i = 0
LOOP:
if (i == R1) goto END
RAM[R0 + i] = -1
i = i + 1
goto LOOP
END:

## Slide 157: Pointer-based processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
Assembly code
Pseudocode
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
// i = 0
@i
M=0
(LOOP)
// if (i == R1) goto END
@i
D=M
@R1
D=D-M
@END
D;JEQ
// RAM[R0 + i] = -1
@R0
D=M
@i
A=D+M
M=-1
// i = i + 1
@i
M=M+1
// goto LOOP
@LOOP
0;JMP
(END)
@END
0;JMP
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
i = 0
LOOP:
if (i == R1) goto END
RAM[R0 + i] = -1
i = i + 1
goto LOOP
END:

## Slide 158: Array processing
300
0
R0
5
1
R1
2
R2
...
...
15
R15
16
i
17
...
255
256
...
–1
300
–1
301
–1
302
–1
303
–1
304
305
...
RAM
desired output
Assembly code
Pseudocode
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
i = 0
LOOP:
if (i == R1) goto END
RAM[R0 + i] = -1
i = i + 1
goto LOOP
END:
// Program: PointerDemo.asm
// Starting at the address stored in R0,
// sets the first R1 words to –1
// i = 0
@i
M=0
(LOOP)
// if (i == R1) goto END
@i
D=M
@R1
D=D-M
@END
D;JEQ
// RAM[R0 + i] = -1
@R0
D=M
@i
A=D+M
M=-1
// i = i + 1
@i
M=M+1
// goto LOOP
@LOOP
0;JMP
(END)
@END
0;JMP
Array processing
Is done similarly, using pointer-based access to the memory block that represents the array.

## Slide 159: Array processing
0
R0
1
R1
2
R2
...
...
15
R15
16
17
...
75
76
...
RAM
255
256
...
5034
5035
5036
5037
5038
5036
...
...
// Declares variables
int[] arr = new int[5];
int sum = 0;
...
// Enters some values into the array
// (code omitted)
...
// Sums up the array elements
for (int j = 0; j < 5; j++) {
sum = sum + arr[j];
}
...
High-level code (e.g. Java)

## Slide 160: Array processing
0
R0
1
R1
2
R2
...
...
15
R15
5034
16
arr
357
17
sum
4
...
j
75
76
...
RAM
255
256
...
100
5034
50
5035
200
5036
2
5037
5
5038
5036
...
...
// Declares variables
int[] arr = new int[5];
int sum = 0;
...
// Enters some values into the array
// (code omitted)
...
// Sums up the array elements
for (int j = 0; j < 5; j++) {
sum = sum + arr[j];
}
...
High-level code (e.g. Java)
Memory state after executing this code:

## Slide 161: Array processing
...
// Declares variables
int[] arr = new int[5];
int sum = 0;
...
// Enters some values into the array
// (code omitted)
...
// Sums up the array elements
for (int j = 0; j < 5; j++) {
sum = sum + arr[j];
}
...
Hack assembly
0
R0
1
R1
2
R2
...
...
15
R15
5034
16
arr
357
17
sum
4
...
j
75
76
...
RAM
255
256
...
100
5034
50
5035
200
5036
2
5037
5
5038
5036
...
Compiler
...
High-level code (e.g. Java)

## Slide 162: Array processing
...
// Declares variables
int[] arr = new int[5];
int sum = 0;
...
// Enters some values into the array
// (code omitted)
...
// Sums up the array elements
for (int j = 0; j < 5; j++) {
sum = sum + arr[j];
}
...
Hack assembly
0
R0
1
R1
2
R2
...
...
15
R15
5034
16
arr
357
17
sum
4
...
j
75
76
...
RAM
255
256
...
100
5034
50
5035
200
5036
2
5037
5
5038
5036
...
Compiler
High-level code (e.g. Java)
...
// sum = sum + arr[j]
@arr
D=M
@j
A=D+M
D=M
@sum
M=M+D
...

## Slide 163: Array processing
...
// Declares variables
int[] arr = new int[5];
int sum = 0;
...
// Enters some values into the array
// (code omitted)
...
// Sums up the array elements
for (int j = 0; j < 5; j++) {
sum = sum + arr[j];
}
...
// Increments each array element
for (int j = 0; j < 5; j++) {
arr[j] = arr[j] + 1
}
...
Hack assembly
0
R0
1
R1
2
R2
...
...
15
R15
5034
16
arr
357
17
sum
4
...
j
75
76
...
RAM
255
256
...
100
5034
50
5035
200
5036
2
5037
5
5038
5036
...
Compiler
High-level code (e.g. Java)
...
// sum = sum + arr[j]
@arr
D=M
@j
A=D+M
D=M
@sum
M=M+D
...

## Slide 164: Array processing
...
// sum = sum + arr[j]
@arr
D=M
@j
A=D+M
D=M
@sum
M=M+D
...
// arr[j] = arr[j] + 1
Hack assembly
0
R0
1
R1
2
R2
...
...
15
R15
5034
16
arr
357
17
sum
4
...
j
75
76
...
RAM
255
256
...
100
5034
50
5035
200
5036
2
5037
5
5038
5036
...
?
High-level code (e.g. Java)
...
// Declares variables
int[] arr = new int[5];
int sum = 0;
...
// Enters some values into the array
// (code omitted)
...
// Sums up the array elements
for (int j = 0; j < 5; j++) {
sum = sum + arr[j];
}
...
// Increments each array element
for (int j = 0; j < 5; j++) {
arr[j] = arr[j] + 1
}
...
Compiler

## Slide 165: Array processing
High-level code (e.g. Java)
...
// Declares variables
int[] arr = new int[5];
int sum = 0;
...
// Enters some values into the array
// (code omitted)
...
// Sums up the array elements
for (int j = 0; j < 5; j++) {
sum = sum + arr[j];
}
...
// Increments each array element
for (int j = 0; j < 5; j++) {
arr[j] = arr[j] + 1
}
...
...
// sum = sum + arr[j]
@arr
D=M
@j
A=D+M
D=M
@sum
M=M+D
...
// arr[j] = arr[j] + 1
@arr
D=M
@j
A=D+M
M=M+1
...
Hack assembly
0
R0
1
R1
2
R2
...
...
15
R15
5034
16
arr
357
17
sum
4
...
j
75
76
...
RAM
255
256
...
100
5034
50
5035
200
5036
2
5037
5
5038
5036
...
Every high-level array access operation involving arr[expression] can be compiled into Hack code that realizes the operation using the low-level memory access instruction A = arr + expression
Compiler

## Slide 166: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 167: The A instruction
A instruction
C instruction
@value
Syntax:
Where value is either:
  a constant, or
  a symbol bound to a constant
Semantics:
Sets the A register to the constant
Side effects:
  RAM[A] becomes the selected RAM register
  ROM[A] becomes the selected ROM register
  Instruction set

## Slide 168: The C instruction
A instruction
C instruction
  Instruction set

## Slide 169: The C instruction
dest = comp ; jump
both dest and jump are optional
Syntax:

## Slide 170: The C instruction
where:
0, 1, –1, D, A, !D, !A, –D, –A, D+1, A+1, D–1, A–1, D+A, D–A, A–D, D&A, D|A
M, !M, –M, M+1, M–1, D+M, D–M, M–D, D&M, D|M
comp =
null, JGT, JEQ, JGE, JLT, JNE, JLE, JMP
jump =
dest = comp ; jump
both dest and jump are optional
Syntax:
null, M, D, DM, A, AM, AD, ADM
dest =
M stands for RAM[A]
Semantics:
Computes the value of comp and stores the result in dest.
If (comp jump 0), jumps to execute ROM[A]

## Slide 171: The C instruction
where:
0, 1, –1, D, A, !D, !A, –D, –A, D+1, A+1, D–1, A–1, D+A, D–A, A–D, D&A, D|A
M, !M, –M, M+1, M–1, D+M, D–M, M–D, D&M, D|M
comp =
null, JGT, JEQ, JGE, JLT, JNE, JLE, JMP
jump =
null, M, D, DM, A, AM, AD, ADM
dest =
dest = comp ; jump
both dest and jump are optional
Syntax:
M stands for RAM[A]
Semantics:
Computes the value of comp and stores the result in dest.
If (comp jump 0), jumps to execute ROM[A]
Examples:
// Sets the D register to -1

## Slide 172: The C instruction
Examples:
// Sets the D register to -1
D=-1
where:
0, 1, –1, D, A, !D, !A, –D, –A, D+1, A+1, D–1, A–1, D+A, D–A, A–D, D&A, D|A
M, !M, –M, M+1, M–1, D+M, D–M, M–D, D&M, D|M
comp =
null, JGT, JEQ, JGE, JLT, JNE, JLE, JMP
jump =
null, M, D, DM, A, AM, AD, ADM
dest =
dest = comp ; jump
both dest and jump are optional
Syntax:
M stands for RAM[A]
Semantics:
Computes the value of comp and stores the result in dest.
If (comp jump 0), jumps to execute ROM[A]

## Slide 173: The C instruction
where:
0, 1, –1, D, A, !D, !A, –D, –A, D+1, A+1, D–1, A–1, D+A, D–A, A–D, D&A, D|A
M, !M, –M, M+1, M–1, D+M, D–M, M–D, D&M, D|M
comp =
null, JGT, JEQ, JGE, JLT, JNE, JLE, JMP
jump =
null, M, D, DM, A, AM, AD, ADM
dest =
dest = comp ; jump
both dest and jump are optional
Syntax:
M stands for RAM[A]
Semantics:
Computes the value of comp and stores the result in dest.
If (comp jump 0), jumps to execute ROM[A]
Examples:
// Sets D and M to the value of the D register, plus 1

## Slide 174: The C instruction
where:
0, 1, –1, D, A, !D, !A, –D, –A, D+1, A+1, D–1, A–1, D+A, D–A, A–D, D&A, D|A
M, !M, –M, M+1, M–1, D+M, D–M, M–D, D&M, D|M
comp =
null, JGT, JEQ, JGE, JLT, JNE, JLE, JMP
jump =
null, M, D, DM, A, AM, AD, ADM
dest =
dest = comp ; jump
both dest and jump are optional
Syntax:
M stands for RAM[A]
Semantics:
Computes the value of comp and stores the result in dest.
If (comp jump 0), jumps to execute ROM[A]
Examples:
// Sets D and M to the value of the D register, plus 1
DM=D+1

## Slide 175: The C instruction
where:
0, 1, –1, D, A, !D, !A, –D, –A, D+1, A+1, D–1, A–1, D+A, D–A, A–D, D&A, D|A
M, !M, –M, M+1, M–1, D+M, D–M, M–D, D&M, D|M
comp =
null, JGT, JEQ, JGE, JLT, JNE, JLE, JMP
jump =
null, M, D, DM, A, AM, AD, ADM
dest =
dest = comp ; jump
both dest and jump are optional
Syntax:
M stands for RAM[A]
Semantics:
Computes the value of comp and stores the result in dest.
If (comp jump 0), jumps to execute ROM[A]
Examples:
// If (D-1 = 0) jumps to execute the instruction stored in ROM[56]

## Slide 176: The C instruction
where:
0, 1, –1, D, A, !D, !A, –D, –A, D+1, A+1, D–1, A–1, D+A, D–A, A–D, D&A, D|A
M, !M, –M, M+1, M–1, D+M, D–M, M–D, D&M, D|M
comp =
null, JGT, JEQ, JGE, JLT, JNE, JLE, JMP
jump =
null, M, D, DM, A, AM, AD, ADM
dest =
dest = comp ; jump
both dest and jump are optional
Syntax:
M stands for RAM[A]
Semantics:
Computes the value of comp and stores the result in dest.
If (comp jump 0), jumps to execute ROM[A]
Examples:
// If (D-1 = 0) jumps to execute the instruction stored in ROM[56]
@56
D-1;JEQ

## Slide 177: Recap: A instructions and C instructions
Observation: C instructions that include both M and a jump directive make no sense
// if D=0 goto 100
@100
D;JEQ
To set up for a C instruction that specifies a jump,
Use an A instruction that selects the memory address to which you want to jump
// RAM[5] = RAM[5] - 1
@5
M=M-1
They normally come in pairs:
To set up for a C instruction that mentions M,
Use an A instruction that selects the memory address on which you want to operate
Best practice rule: Each C instruction should …
Either have a reference to M
Or have a jump directive
But not both.

## Slide 178: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 179: The Hack machine language
So far, we illustrated the Hack language using examples.
We now turn to give a complete language specification.

## Slide 180: Hack machine language
RAM
ROM
instructions
data out
data in
CPU
Binary code
...
@17
D;JLE
...
Symbolic: (example)
load & execute
translate
...
0000000000010001
1110001100000110
...
Binary:
The Hack language:
The binary version of the language is not essential for low-level programming
We present it anyway, for completeness
The binary version will come to play when we’ll build the computer architecture (chapter 5) and the assembler (chapter 6)

## Slide 181: A instruction
Action: Sets the A register to a constant
@6
Symbolic:
Example:
Where value is either:
  a non-negative decimal constant ≤ 32767 ( = 215 – 1)
  or a symbol bound to a constant
@value
Symbolic syntax:
0000000000000110
Binary:
Binary syntax:
0vvvvvvvvvvvvvvvv
Where:
  0 is the A instruction op-code
  v v v … v is the 15-bit binary representation of the constant

## Slide 182: C instruction
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Symbolic syntax:
dest = comp ; jump
Binary syntax:
comp is mandatory.
If dest is empty, the = is omitted; If jump is empty, the ; is omitted
1 1 1 a c c c c c c d d d j j j

## Slide 183: C instruction
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Symbolic syntax:
dest = comp ; jump
comp is mandatory.
If dest is empty, the = is omitted; If jump is empty, the ; is omitted
Binary syntax:
dest bits
jump bits
comp bits
not used
1 1 1 a c c c c c c d d d j j j
C instruction op-code

## Slide 184: C instruction
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
–1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
–D |  | 0 | 0 | 1 | 1 | 1 | 1
–A | –M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D–1 |  | 0 | 0 | 1 | 1 | 1 | 0
A–1 | M–1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D–A | D–M | 0 | 1 | 0 | 0 | 1 | 1
A–D | M–D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
comp bits
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Symbolic syntax:
dest = comp ; jump
comp is mandatory.
If dest is empty, the = is omitted; If jump is empty, the ; is omitted
Binary syntax:
1 1 1 a c c c c c c d d d j j j

## Slide 185: C instruction
dest bits
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Symbolic syntax:
dest = comp ; jump
comp is mandatory.
If dest is empty, the = is omitted; If jump is empty, the ; is omitted
Binary syntax:
1 1 1 a c c c c c c d d d j j j

## Slide 186: C instruction
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
jump bits
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
Symbolic syntax:
dest = comp ; jump
comp is mandatory.
If dest is empty, the = is omitted; If jump is empty, the ; is omitted
1 1 1 a c c c c c c d d d j j j
Binary syntax:

## Slide 187: The Hack language specification
A instruction
(vv ... v = 15-bit value of xxx)
(xxx is a decimal value ranging from 0 to 32767, or a symbol bound to such a decimal value)
Symbolic:
@xxx
Binary:
0 vvvvvvvvvvvvvvv
dest = comp; jump
111accccccdddjjj
(comp is mandatory. If dest is empty, the = is omitted; If jump is empty, the ; is omitted)
C instruction
Symbolic:
Binary:
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
–1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
–D |  | 0 | 0 | 1 | 1 | 1 | 1
–A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D–1 |  | 0 | 0 | 1 | 1 | 1 | 0
A–1 | M–1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D–A | D–M | 0 | 1 | 0 | 0 | 1 | 1
A–D | M–D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register (reg)
DM | 0 | 1 | 1 | RAM[A] and D reg
A | 1 | 0 | 0 | A reg
AM | 1 | 0 | 1 | A reg and RAM[A]
AD | 1 | 1 | 0 | A reg and D reg
ADM | 1 | 1 | 1 | A reg, D reg, and RAM[A]
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | unconditional jump
comp c c c c c c
a == 0 a == 1
dest d d d Effect: store comp in:
jump j j j Effect:

## Slide 188: The Hack language specification
A instruction
(vv ... v = 15-bit value of xxx)
(xxx is a decimal value ranging from 0 to 32767, or a symbol bound to such a decimal value)
Symbolic:
@xxx
Binary:
0 vvvvvvvvvvvvvvv
dest = comp; jump
111accccccdddjjj
(comp is mandatory. If dest is empty, the = is omitted; If jump is empty, the ; is omitted)
C instruction
Symbolic:
Binary:
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
–1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
–D |  | 0 | 0 | 1 | 1 | 1 | 1
–A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D–1 |  | 0 | 0 | 1 | 1 | 1 | 0
A–1 | M–1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D–A | D–M | 0 | 1 | 0 | 0 | 1 | 1
A–D | M–D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register (reg)
DM | 0 | 1 | 1 | RAM[A] and D reg
A | 1 | 0 | 0 | A reg
AM | 1 | 0 | 1 | A reg and RAM[A]
AD | 1 | 1 | 0 | A reg and D reg
ADM | 1 | 1 | 1 | A reg, D reg, and RAM[A]
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | unconditional jump
comp c c c c c c
a == 0 a == 1
dest d d d Effect: store comp in:
jump j j j Effect:
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
SCREEN | 16384
KBD | 24576
Predefined symbols:

## Slide 189: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 190: Input / output
data
RAM
ROM
instruc-
tions
CPU
  Keyboard: used to enter inputs
  Screen: used to display outputs
Hello, world
Low-level I/O handling:
Manipulating bits in memory resident bitmaps.
High-level I/O handling:
Software libraries for inputting / outputting text, graphics, audio, video, …
Notes: Input: loading selected RAM registers with values
Output: inspecting the state of selected RAM registers

## Slide 191: Bitmaps
0
...
15
16
...
255
256
...
RAM
2047
2048
...
16383
16384
...
24575
24576
...
32767
Hello, world

## Slide 192: Bitmaps
0
...
15
16
...
255
256
...
RAM
2047
2048
...
16383
screen memory map
16384
...
24575
keyboard
24576
...
32767
Hello, world

## Slide 193: Bitmaps
0
...
15
16
...
255
256
...
RAM
2047
2048
...
16383
screen memory map
16384
...
24575
24576
...
32767
Hello, world
Screen memory map:
An 8K memory block, dedicated to representing a black-and-white display unit
Base address: SCREEN = 16384 (predefined symbol)
Output is effected by writing bits in the screen memory map.
SCREEN =

## Slide 194: Bitmaps
...
...
...
...
...
Screen shots of computer games developed on the Hack computer
Physical screen

## Slide 195: Bitmaps
...
...
...
...
...
Screen shots of computer games developed on the Hack computer
Physical screen

## Slide 196: Bitmaps
...
...
...
...
...
Screen shots of computer games developed on the Hack computer
Physical screen

## Slide 197: Bitmaps
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen

## Slide 198: Bitmaps
refresh
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191
Screen Memory Map
row 0
. . .
row 255
row 1
16384
base address of the screen memory map
SCREEN
=
Mapping:
The pixel in location (row, col) in the physical screen is represented by the (col % 16)th bit in RAM address SCREEN + 32*row + col/16

## Slide 199: Bitmaps
refresh
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
To set pixel (row , col) to black or white:
addr ← SCREEN + 32*row + col/16
word ← RAM[addr]
(2) Set the (col % 16)th bit of word to 0 or 1
RAM[addr] ← word
Not to worry:
Nice workarounds coming up
(Bitmap Editor)
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191
Screen Memory Map
row 0
. . .
row 255
row 1
16384
base address of the screen memory map
SCREEN
=

## Slide 200: Bitmaps
refresh
Examples of simple patterns that can be drawn relatively easily:
// Sets the first (left) 16 pixels
// of the top row to black
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191
Screen Memory Map
row 0
. . .
row 255
row 1
16384
base address of the screen memory map
SCREEN
=

## Slide 201: Bitmaps
refresh
Examples of simple patterns that can be drawn relatively easily:
// Sets the first (left) 16 pixels
// of the top row to black
@SCREEN
M=-1 // –1 = 1111111111111111
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
// Sets the first 16 pixels
// of row 2 to black
?
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191
Screen Memory Map
row 0
. . .
row 255
row 1
16384
base address of the screen memory map
SCREEN
=

## Slide 202: Bitmaps
refresh
Examples of simple patterns that can be drawn relatively easily:
// Sets the first (left) 16 pixels
// of the top row to black
@SCREEN
M=-1 // –1 = 1111111111111111
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
// Sets the first 16 pixels
// of row 2 to black
@64
D=A
@SCREEN
A=A+D
M=-1
// Sets the entire screen
// to black / white
(Project 4)
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191
Screen Memory Map
row 0
. . .
row 255
row 1
16384
base address of the screen memory map
SCREEN
=

## Slide 203: Bitmaps
refresh
Examples of simple patterns that can be drawn relatively easily:
// Sets the first (left) 16 pixels
// of the top row to black
@SCREEN
M=-1 // –1 = 1111111111111111
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
Simple graphics program:
Rectangle
Drawing
demo
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191
Screen Memory Map
row 0
. . .
row 255
row 1
16384
base address of the screen memory map
SCREEN
=

## Slide 204: Bitmap Editor
0000111111100000 = 4064
0001100000110000 = 6192
0001001010010000 = 4752
...
...
0111111011111100 = 32508
Bitmap editor: A productivity tool for developers.
The developer draws a pixled image on a 2D grid, and the program generates code that draws the image in the RAM.
The generated code can be copy-pasted into the developer’s assembly code.
The Nand to Tetris Bitmap Editor is available in this Git project
Note: The editor generates either Jack code or Hack assembly code – see the radio buttons at the very bottom of the editor’s GUI.

## Slide 205: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 206: Input
data
RAM
ROM
instruc-
tions
CPU
  Keyboard: used to enter inputs
Low-level input handling
Read bits.
High-level input handling
readInt, readString, ...

## Slide 207: Hack RAM
0
...
15
16
...
255
256
...
RAM
2047
2048
...
16383
screen
16384
...
24575
keyboard
24576
...
32767
Hello, world

## Slide 208: Hack RAM
0
...
15
16
...
255
256
...
RAM
2047
2048
...
16383
16384
...
24575
keyboard
24576
...
32767
kbd =
Keyboard memory map
A single 16-bit register, dedicated to representing the keyboard
Base address: KBD = 24576 (predefined symbol)
Reading inputs is affected by probing this register.

## Slide 209: The Hack character set
key | code
(space) | 32
! | 33
“ | 34
# | 35
$ | 36
% | 37
& | 38
‘ | 39
( | 40
) | 41
* | 42
+ | 43
, | 44
- | 45
. | 46
/ | 47
key | code
0 | 48
1 | 49
… | …
9 | 57
: | 58
; | 59
< | 60
= | 61
> | 62
? | 63
@ | 64
key | code
A | 65
B | 66
C | …
… | …
Z | 90
[ | 91
/ | 92
] | 93
^ | 94
_ | 95
` | 96
key | code
a | 97
b | 98
c | 99
… | …
z | 122
key | code
newline | 128
backspace | 129
left arrow | 130
up arrow | 131
right arrow | 132
down arrow | 133
home | 134
end | 135
Page up | 136
Page down | 137
insert | 138
delete | 139
esc | 140
f1 | 141
. . . | . . .
f12 | 152
{ | 123
¦ | 124
} | 125
~ | 126
(Subset of Unicode)

## Slide 210: Memory mapped input
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=

## Slide 211: Memory mapped input
When a key is pressed on the keyboard, the key’s character code appears in the keyboard memory map.
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=
k
code('k') = 75
0000000001001011

## Slide 212: Memory mapped input
When a key is pressed on the keyboard, the key’s character code appears in the keyboard memory map.
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=
4
code('4') = 52
0000000000110100

## Slide 213: Memory mapped input
When a key is pressed on the keyboard, the key’s character code appears in the keyboard memory map.
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=

code('') = 131
0000000010000011

## Slide 214: Memory mapped input
When a key is pressed on the keyboard, the key’s character code appears in the keyboard memory map.
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=
space
code(' ') = 32
0000000000100000

## Slide 215: Memory mapped input
0000000000000000
RAM
When no key is pressed, the resulting code is 0.
24576
base address of the keyboard memory map
KBD
=

## Slide 216: Reading inputs
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=
k
code('k') = 75
0000000001001011
// Set D to the character code of
// the currently pressed key
Examples:

## Slide 217: Reading inputs
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=
k
code('k') = 75
0000000001001011
// Set D to the character code of
// the currently pressed key
@KBD
D=M
Examples:
// If the currently pressed key is 'q', goto END

## Slide 218: Reading inputs
0000000000000000
RAM
24576
base address of the keyboard memory map
KBD
=
k
code('k') = 75
0000000001001011
// Set D to the character code of
// the currently pressed key
@KBD
D=M
Examples:
// If the currently pressed key is 'q', goto END
@KBD
D=M
@113 // 'q'
D=D-A
@END
D;JEQ

## Slide 219: Chapter 4: Machine Language
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Machine languages
  The Hack computer
  The Hack instruction set
  The Hack CPU Emulator
  The Hack Language
  Usage
  Specification
  Output
  Input
  Project 4
  Low Level Programming
  Basic
  Iteration
  Pointers

## Slide 220: Project 4
Objectives
Gain a hands-on taste of:
Low-level programming
Assembly language
The Hack computer
Tasks
Write a simple algebraic program: Mult
Write a simple interactive program: Fill
Be creative: Define and write some program of your own.

## Slide 221: Mult: a program that computes R2 = R0 * R1
code not shown

## Slide 222: Mult: a program that computes R2 = R0 * R1
code not shown

## Slide 223: Mult: a program that computes R2 = R0 * R1
code not shown
Implementation strategy
Loop: Repetitive addition
Inefficient implementation of multiplication, but OK for the purpose of this project.

## Slide 224: Fill: a simple interactive program
code not shown
code not shown
When the user presses a keyboard key (any key), the entire screen becomes black

## Slide 225: Fill: a simple interactive program
code not shown
code not shown
The screen remains black as long as the key is pressed.

## Slide 226: Fill: a simple interactive program
code not shown
code not shown
When the user releases the key, the screen is cleared

## Slide 227: Fill: a simple interactive program
code not shown
code not shown

## Slide 228: Fill: a simple interactive program
code not shown
code not shown
Etc...

## Slide 229: Fill: a simple interactive program
code not shown
code not shown
Etc...

## Slide 230: Fill: a simple interactive program
Implementation strategy
Execute an infinite loop that listens to the keyboard input
When a key is pressed (any key), execute code that writes "black" in every pixel
When no key is pressed, execute code that writes "white" in every pixel
​Tip: This program requires working with pointers.

## Slide 231: Program development process
happy with results?
Find and fix the errors
No
Load the program into the CPU emulator, and run it
Yes
Write / edit the program using a text editor
Prog.asm
Translation options
1. Let the CPU emulator translate into binary code (as seen on the left)
2. Use the supplied assembler:
Find it on your PC in nand2tetris/tools
See the Assembler Tutorial in Project 6 (www.nand2tetris.org)

## Slide 232: Implementation notes
Well-written low-level code is
Compact
Efficient
Elegant
Self-describing
Tips
Use symbolic variables and labels
Use sensible variable and label names
Variables: lower-case
Labels: upper-case
Use indentation
Start by writing pseudocode.

## Slide 233: Task 3:Define and write a program of your own
Any ideas?
It’s your call!

## Slide 234: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
p4
Writing low-level programs
This lecture:
The Hack computer / instruction set
Low-level programming
Assembly / assemblers

## Slide 235: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
p4
Writing low-level programs
This lecture:
The Hack computer / instruction set
Low-level programming
Assembly / assemblers
Next lecture
p5