## Slide 1
Chapter 5
Computer Architecture
From Nand to Tetris
Building a Modern Computer from First Principles
These slides support chapter 5 of the book
The Elements of Computing Systems
(1st and 2nd editions)
By Noam Nisan and Shimon Schocken
MIT Press

## Slide 2: Usage Notice
  You are welcome to use this presentation, or any part of it, in Nand to Tetris courses, or in other courses, as you see fit.
  Usage is free provided that it supports instruction in educational, non-profit settings.
  You can use the slides as-is, or modify them as needed.
  We’ll appreciate it if you will credit Nand to Tetris somewhere, and put a reference to www.nand2tetris.org
  Happy teaching!
  Shimon Schocken / Noam Nisan

## Slide 3: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler

## Slide 4: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
p4
Writing low-level programs
Previous chapter:
Low-level programming
Assembly language
Hack computer overview

## Slide 5: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
p4
Writing low-level programs
p5
This chapter: Integrate the chips built in chapters 1,2,3 into a computer architecture capable of executing programs written in the machine language introduced in chapter 4

## Slide 6: Nand to Tetris Roadmap (Part I: Hardware)
Machine language program (example)
// Computes R1 = 1 + 2 + 3 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if (i > R0) goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
...
Register
16
16
PC
16
16
RAM
16
16
14
ALU
x
f
16
y
16
out
16
This chapter: Integrate the chips built in chapters 1,2,3 into a computer architecture capable of executing programs written in the machine language introduced in chapter 4

## Slide 7: Computer architecture
program
Memory
CPU
data
PC



data register
address register
ALU
data register
data register
input
output
Typical computer architecture:
Stored program concept
General-purpose
In this chapter we build the Hack computer – a variant of this architecture.

## Slide 8: Chapter 5: Computer Architecture
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines

## Slide 9: Chapter 5: Computer Architecture
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines

## Slide 10: Early computers (17th century)
Blaise Pascal 1623-1662
Pascal’s Calculator
(Pascaline, 1652)
Add
Subtract

## Slide 11: Early computers (17th century)
Gottfried Leibniz 1646-1716
Leibniz Calculator (1673)
Add
Subtract
Multiply
Divide.

## Slide 12: Early computers (17th century)
Gottfried Leibniz 1646-1716
Leibniz Calculator (1673)
Add
Subtract
Multiply
Divide.
Side benefits: Advances in gears / mechanical engineering

## Slide 13: Early computers (19th century)
Jacquard Loom (1804)
Analytic Engine (1837)
Major innovation:
Punched cards = software

## Slide 14: Early computers
17th century: Hardware only / fixed / single purpose
Programmable!
19th century: Hardware / Software / General purpose

## Slide 15: Modern computers (20th century)
ENIAC: First digital, programmable, stored program computer
University of Pennsylvania, 1946,
(Borrowed key ideas from other early computers and innovators)
John Von Neumann

## Slide 16: Modern computers (20th century)
John Von Neumann
John Atanassof
Konrad Zuse
Howard Aiken
John Mauchly
Presper Eckert
Tommy Flowers
Colossus: First digital, programmable, computer, UK, 1945
ENIAC: First digital, programmable, stored program computer
University of Pennsylvania, 1946,
(Borrowed key ideas from other early computers and innovators)

## Slide 17: Modern computers (20th century)
Kathleen McNulty, Jean Jennings, Frances Snyder, Marlyn Wescoff, Frances Bilas, Ruth Lichterman
Adele Koss
Grace Hopper
Compilation pioneers
(Mark I)
ENIAC Women
Pioneered reusable code, subroutines, flowcharts, and many other programming innovations

## Slide 18: Modern computers (20th century)
Same hardware can run many different programs (software)
Back in the 1950’s, this was considered a radical idea:
“If it should turn out that the basic logic of a machine designed for the numerical solution of differential equations coincides with the logic of a machine intended to make bills for department stores, I would regard this as the most amazing coincidence I have ever encountered” –– Howard Aiken, 1956 (Mark 1 computer architect)

## Slide 19: Basic architecture
Memory
CPU
register



ALU
register
register
input
output
program
data
Stored program concept:
Same machine can run different programs
“The stored program computer, as conceived by Alan Turing and delivered by John von Neumann, broke the distinction between numbers that mean things and numbers that do things. Our universe would never be the same”. (George Dyson)

## Slide 20: Basic architecture
program
Memory
CPU
data
PC



data register
address register
ALU
data register
data register
The computer is essentially a machine that manipulates registers under program control: data registers, address registers, a program counter (PC), memory registers (containing data and instructions).
How does information flow inside the computer?

## Slide 21: Basic architecture
program
Memory
CPU
data
PC



data register
address register
control bus
ALU
data register
data register
instructions

## Slide 22: Basic architecture
program
Memory
CPU
data
PC



data register
address register
control bus
data register
data register
instructions
ALU
address bus
addresses

## Slide 23: Basic architecture
program
Memory
CPU
data
PC



data register
address register
control bus
data register
data register
instructions
data values
ALU
address bus
addresses
data bus
ALU

## Slide 24: Basic architecture: Recap
program
Memory
CPU
data
PC



data register
address register
ALU
data register
data register
General purpose computer
A set of chips connected by buses
Stored program concept
Framework of most modern computers

## Slide 25: Chapter 5: Computer Architecture
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines

## Slide 26: Computer architecture
program
Memory
CPU
data
PC



data register
address register
data register
data register
ALU
Basic loop:
Fetch an instruction (by supplying an address)
Execute the instruction
(And… figure out the address of the next instruction)

## Slide 27: Computer architecture
program
Memory
CPU
data
PC



data register
address register
data register
data register
Program Counter: Always emits the address of the next instruction
ALU
Basic loop:
Fetch an instruction (by supplying an address)
Execute the instruction
(And… figure out the address of the next instruction)

## Slide 28: Fetch an instruction
program
Memory
CPU
data
PC



data register
address register
data register
data register
Program Counter: Always emits the address of the next instruction
instruction
address bus
address
address
ALU
Basic loop:
Fetch an instruction (by supplying an address)
Execute the instruction
(And… figure out the address of the next instruction)

## Slide 29: Fetch an instruction
program
Memory
CPU
data
PC



data register
address register
control bus
data register
data register
ALU
instruction
instruction
Basic loop:
Fetch an instruction (by supplying an address)
Execute the instruction
(And… figure out the address of the next instruction)

## Slide 30: Execute the instruction
program
Memory
CPU
data
PC



data register
address register
control bus
data register
data register
ALU
instruction
instruction
Basic loop:
Fetch an instruction (by supplying an address)
Execute the instruction
(And… figure out the address of the next instruction)
The instruction bits specify:
Which operation to execute
Which address in memory the operation should act on

## Slide 31: Fetch – execute issues
program
Memory
data
control bus
address bus
Which of the two addresses to feed into the Memory’s single address input?
ALU
out
address
data
instruction
data
address
instruc. address
Should the single Memory output be interpreted as data, or as instruction?
Possible solutions:
Two-cycle machine
One-cycle, two-memory machine
(for the instruc. to operates on)

## Slide 32: Two-cycle machine
program
Memory
data
control bus
address bus
ALU
out
address
data
address
instruc. address
data
instruction
(for the instruc. to operates on)

## Slide 33: Two-cycle machine
program
Memory
data
Mux
control bus
address bus
out
ALU
when executing
instruction register
when fetching
DMux
(when executing)
(when fetching)
address
data
address
instruc. address
data
instruction
(for the instruc. to operates on)

## Slide 34: Two-cycle machine
program
Memory
data
ALU
control bus
address bus
out
address
when executing
fetch / execute bit
Fetch cycle: Loads an instruction into the instruction register
Execute cycle: Loads a data value from memory, and executes the instruction
when fetching
data
address
instruc. address
(when executing)
(when fetching)
data
instruction
(for the instruc. to operates on)
Mux
instruction register
DMux

## Slide 35: Single cycle, two-memory machine
Program and data are stored in two separate physical memories
Both memories are accessed simultaneously, in the same cycle
(Sometimes called ”Harvard architecture”)
program
Instruction Memory
CPU
PC



data register
address register
ALU
data register
data register
Data Memory
data
address
instruc-
tion
write
read
address

## Slide 36: Single cycle, two-memory machine
Advantages
Simpler architecture
Faster processing
Disadvantages
Two memory chips
Separate address spaces
program
Instruction Memory
CPU
PC



data register
address register
ALU
data register
data register
Data Memory
data
address
instruc-
tion
write
read
address

## Slide 37: Chapter 5: Computer Architecture
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines

## Slide 38: Hack computer
program
Instruction Memory
CPU
PC
ALU
A register
D register
Data Memory
data
address
instruc-
tion
write
read
address
Hello, world
Single cycle computer
Two separate memory units

## Slide 39: Hack computer
program
Instruction Memory
CPU
PC
ALU
A register
D register
Data Memory
data
address
instruc-
tion
write
read
address
Hello, world

## Slide 40: CPU abstraction
D register
A register
// D = RAM[5] + 1
@5
D=M+1
…
// RAM[3] = D
@3
M=D
…
Instruction examples:
CPU Abstraction:
Executes instructions written in the Hack machine language

## Slide 41: CPU abstraction
Hack instructions (formal specification)

## Slide 42: CPU abstraction
D register
A register
CPU Abstraction:
Executes instructions written in the Hack machine language
// D = RAM[5] + 1
@5
D=M+1
…
// RAM[3] = D
@3
M=D
…
Instruction examples:
Note that the selected memory register M can be input, or output, or both input and output (example: M=M+1)

## Slide 43: CPU abstraction
D register
A register
Holds the value of M, the selected memory register
// D = RAM[5] + 1
@5
D=M+1
…
// RAM[3] = D
@3
M=D
…
Instruction examples:
CPU Abstraction:
Executes instructions written in the Hack machine language
Note that the selected memory register M can be input, or output, or both input and output (example: M=M+1)

## Slide 44: CPU abstraction
D register
A register
Hold the value, write enable bit, and address of M, the selected memory register
// D = RAM[5] + 1
@5
D=M+1
…
// RAM[3] = D
@3
M=D
…
Instruction examples:
Holds the value of M, the selected memory register
CPU Abstraction:
Executes instructions written in the Hack machine language
Note that the selected memory register M can be input, or output, or both input and output (example: M=M+1)

## Slide 45: CPU abstraction
D register
A register
We mention these internal chip-parts (D and A) in the CPU abstraction, since Hack instructions refer to them
// D = RAM[5] + 1
@5
D=M+1
…
// RAM[3] = D
@3
M=D
…
Instruction examples:
Holds the value of M, the selected memory register
CPU Abstraction:
Executes instructions written in the Hack machine language
Note that the selected memory register M can be input, or output, or both input and output (example: M=M+1)
Hold the value, write enable bit, and address of M, the selected memory register

## Slide 46: CPU abstraction
D register
A register
// D = RAM[5] + 1
@5
D=M+1
…
// RAM[3] = D
@3
M=D
…
CPU operation:
1. Executes the instruction:
If it’s an A instruction (@xxx), sets the A register to xxx
Else:
  If the instruction uses M as input, gets this value from inM
  Computes the ALU function specified by the instruction
  If the instruction writes to M, puts the ALU output in outM, puts the register’s address in addressM, and asserts the writeM bit
2. Figures out the address of the next instruction, and puts it in pc.
Instruction examples:

## Slide 47: CPU implementation
pc
Notes: It’s a very lean ALU, consisting of 2 registers, named D and A, a program counter, an ALU, and few more trivial gates.

## Slide 48: CPU implementation
pc
In the diagram, “c“ denotes “control bit”;
The control bits come from the instruction;
They tell the various chip-parts what to do.
Notes: It’s a very lean ALU, consisting of 2 registers, named D and A, a program counter, an ALU, and few more trivial gates.

## Slide 49: CPU implementation
pc
Notes: It’s a very lean ALU, consisting of 2 registers, named D and A, a program counter, an ALU, and few more trivial gates.

## Slide 50: CPU implementation: Instruction handling
writeM
outM
Handling A-instructions
Routes the instruction’s MSB (op-code) to the Mux16 control bit
0000000000000101
@5
inM

## Slide 51: CPU implementation: Instruction handling
writeM
outM
Handling A-instructions
Routes the instruction’s MSB (op-code) to the Mux16 control bit
0000000000000101
@5
inM
0

## Slide 52: CPU implementation: Instruction handling
writeM
outM
Handling A-instructions
Routes the instruction’s MSB (op-code) to the Mux16 control bit
0000000000000101
@5
inM
0
Result: A-register  instruction (value)
(Exactly what the @xxx instruction specifies: “set A to xxx”)

## Slide 53: CPU implementation: Instruction handling
writeM
outM
inM
1110011111010111
D=D+1;JMP

## Slide 54: CPU implementation: Instruction handling
writeM
outM
inM
  opcode bit
  comp bits
  dest bits
  jump bits
1110011111010111
D=D+1;JMP
Handling C-instructions
Each instruction field (opcode, comp bits, dest bits, and jump bits) is handled separately
Each group of bits is used to ”tell” a CPU chip-part what to do
Taken together, the chip-parts end up executing the instruction.

## Slide 55: CPU implementation: Instruction handling
writeM
outM
inM
Handling C-instructions (the opcode bit):
Routes the instruction’s MSB to the Mux16
Result: Prepares the A register to get the ALU output.
1
  opcode bit
  comp bits
  dest bits
  jump bits
1110011111010111
D=D+1;JMP

## Slide 56: CPU implementation: Instruction handling
writeM
1110011111010111
outM
011111
0
Result: the ALU computes the specified function
which becomes the ALU output
Handling C-instructions (the computation bits)
Routes the instruction’s c-bits to the ALU control bits
Routes the instruction’s a-bit to the Mux16
inM
  opcode bit
  comp bits
  dest bits
  jump bits
D=D+1;JMP

## Slide 57: CPU implementation: Instruction handling
writeM
outM
inM
ALU output:
Result of ALU calculation
1110011111010111
  opcode bit
  comp bits
  dest bits
  jump bits
D=D+1;JMP

## Slide 58: CPU implementation: Instruction handling
writeM
outM
ALU output:
Result of ALU calculation
Fed simultaneously to D-register, A-register, data memory
inM
  opcode bit
  comp bits
  dest bits
  jump bits
1110011111010111
D=D+1;JMP

## Slide 59: CPU implementation: Instruction handling
writeM
outM
ALU output:
Result of ALU calculation
Fed simultaneously to D-register, A-register, data memory
All enabled/disabled by control bits
inM
  opcode bit
  comp bits
  dest bits
  jump bits
1110011111010111
D=D+1;JMP

## Slide 60: CPU implementation: Instruction handling
writeM
1110011111010111
outM
0
1
0
Handling C-instructions (the destination bits)
Routes the instruction's d-bits to the control (load) bits of the A-register, D-register, and to the writeM bit
Result: Only the enabled destinations get the ALU output
inM
  opcode bit
  comp bits
  dest bits
  jump bits
D=D+1;JMP

## Slide 61: CPU implementation: Instruction handling
writeM
1110011111010111
outM
011111
0
1
Executes dest = comp
Figures out which instruction to execute next
Handling C-instructions (recap)
0
1
0
inM
  opcode bit
  comp bits
  dest bits
  jump bits
D=D+1;JMP

## Slide 62: CPU implementation: Control
Symbolic
syntax:
dest = comp ; jump
1 1 1 a c c c c c c d d d j1 j2 j3
Binary
syntax:

## Slide 63: CPU implementation: Control
jump | j1 | j2 | j3 | condition
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if (ALU out > 0) jump
JEQ | 0 | 1 | 0 | if (ALU out = 0) jump
JGE | 0 | 1 | 1 | if (ALU out ≥ 0) jump
JLT | 1 | 0 | 0 | if (ALU out < 0) jump
JNE | 1 | 0 | 1 | if (ALU out ≠ 0) jump
JLE | 1 | 1 | 0 | if (ALU out ≤ 0) jump
JMP | 1 | 1 | 1 | Unconditional jump
ALU
f
out
zr
ng
if (out == 0) zr = 1, else zr = 0
if (out < 0) ng = 1, else ng = 0
Jump decision:
J (j1, j2, j3, zr, ng) = 1 if condition is true, 0 otherwise
J can be computed using gate logic,
And then help compute the address of the next instruction
Symbolic
syntax:
1 1 1 a c c c c c c d d d j1 j2 j3
Binary
syntax:
dest = comp ; jump

## Slide 64: CPU implementation: Control
pc
zr
ng
address of next instruction
How to compute it?
Notes: Which instruction should be executed next?

## Slide 65: CPU implementation: Control
load
16
1
16
111accccccdddjjj
...
address of next instruction
pc
zr
ng
PC (program counter) abstraction:
Outputs the address of the next instruction:
reset: PC  0
no jump: PC++
jump: if (condition) PC  A // A contains the address of the
// jump destination
Notes: The bottom line of this whole apparatus is the address of the next instruction
Assumption: if the j-bits code a goto directive, then we assume that the A register was previously set to the goto address

## Slide 66: CPU implementation: Control
load
16
1
16
...
pc
load
zr
ng
PC (program counter) implementation:
if (reset == 1) PC  0 // reset
else
if ( J(jump bits, zr, ng) == 1) PC  A // jump
else PC++ // next instruction
111accccccdddjjj
address of next instruction
Notes: The bottom line of this whole apparatus is the address of the next instruction
Assumption: if the j-bits code a goto directive, then we assume that the A register was previously set to the goto address

## Slide 67: CPU implementation
pc
Executes the current instruction
Figures out which instruction to execute next.
Notes: Which instruction should be executed next?

## Slide 68: Chapter 5: Computer Architecture
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines

## Slide 69: Hack computer
I/O devices
Screen (black and white)
Keyboard (regular)
program
Instruction Memory
CPU
PC
ALU
A register
D register
Data
Data Memory
address
instruc-
tion
write
read
address
keyboard mem. map
Hello, world
screen memory map

## Slide 70: Screen
refresh
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
Screen memory map
Screen
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191

## Slide 71: Screen
Screen
load
The screen memory map is implemented as an 8K memory chip named Screen
1111010100000000
0000000000000000
0000000000000001
0
1
. . .
31
0000101000000000
0000000000000000
0000000000000000
32
33
. . .
63
. . .
1011010100000000
0000000000000000
0000000000000000
8159
8160
. . .
8191
in
16
address
13
out
16
/** Memory of 8K 16-bit registers
with a display-unit side effect. */
CHIP Screen {
IN address[13], in[16], load;
OUT out[16];
BUILTIN Screen;
CLOCKED in, load;
}
Screen
...
0
1
2
3
4
5
6
7
8
...
511
0
1
...
...
...
...
255
Physical screen
refresh

## Slide 72: Hack computer
I/O devices
Screen (black and white)
Keyboard (regular)
program
Instruction Memory
CPU
PC
ALU
A register
D register
Data
Data Memory
address
instruc-
tion
write
read
address
keyboard mem. map
Hello, world
screen memory map

## Slide 73: Keyboard
0000000000000000
Keyboard
out
16
refresh

## Slide 74: Keyboard
0000000000000000
Keyboard
k
code('k') = 75
0000000001001011
out
16
refresh

## Slide 75: Keyboard
0000000000000000
Keyboard
refresh
out
16
/** 16-bit register that outputs the character code of the currently pressed keyboard key, or 0 if no key is pressed */
CHIP Keyboard {
OUT
out[16];
BUILTIN Keyboard;
}
The keyboard memory map is implemented as a 16-bit memory register named Keyboard

## Slide 76: The Hack character set
key | code
(space) | 32
! | 33
“ | 34
# | 35
$ | 36
% | 37
& | 38
‘ | 39
( | 40
) | 41
* | 42
+ | 43
, | 44
- | 45
. | 46
/ | 47
key | code
0 | 48
1 | 49
… | …
9 | 57
: | 58
; | 59
< | 60
= | 61
> | 62
? | 63
@ | 64
key | code
A | 65
B | 66
C | …
… | …
Z | 90
[ | 91
/ | 92
] | 93
^ | 94
_ | 95
` | 96
key | code
a | 97
b | 98
c | 99
… | …
z | 122
key | code
newline | 128
backspace | 129
left arrow | 130
up arrow | 131
right arrow | 132
down arrow | 133
home | 134
end | 135
Page up | 136
Page down | 137
insert | 138
delete | 139
esc | 140
f1 | 141
. . . | . . .
f12 | 152
{ | 123
¦ | 124
} | 125
~ | 126
(Subset of Unicode)

## Slide 77: Hack computer
program
Instruction Memory
CPU
PC
ALU
A register
D register
Data Memory
address
instruc-
tion
write
read
address
Hello, world
screen memory map
keyboard mem. map
I/O devices
Screen (black and white)
Keyboard (regular)
More I/O devices can be added, as needed
Each requiring a memory map, and an interaction contract
Managed jointly by the hardware and the OS.

## Slide 78: Chapter 5: Computer Architecture
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines

## Slide 79: Chapter 5: Computer Architecture
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output

## Slide 80: Memory
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Intro
  Computer architecture
  The Hack CPU
  Input / output
  Memory
program
Instruction Memory
CPU
PC
ALU
A register
D register
Data
Data Memory
address
instruc-
tion
write
read
address
Hello, world

## Slide 81: Memory: Abstraction
Memory
in
16
1
0
24576
address
15
out
16
load
2
...
Reading register i:
address  i
Probe out
Setting register i to v:
in  v
address  i
load  1

## Slide 82: Memory: Implementation
Memory
in
16
RAM16K
16383
0
Keyboard
24576
24575
16384
Screen
(8K)
address
15
out
16
load
screen memory map
keyboard memory map
data
Reading register i:
address  i
Probe out
Setting register i to v:
in  v
address  i
load  1

## Slide 83: Memory: Implementation
RAM16K
in
16
address
14
out
16
built in project 3
Memory architecture
An aggregate of three chip-parts: RAM16K, Screen, Keyboard
Single address space, 0 to 24576
Maps the address input onto the corresponding address input of the relevant chip-part.
Keyboard
out
16
built-in chip
in
16
address
13
out
16
Screen
Hello, world
built-in chip
Memory
in
16
RAM16K
16383
0
Keyboard
24576
24575
16384
Screen
(8K)
address
15
out
16
load

## Slide 84: Instruction memory
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Intro
  Computer architecture
  The Hack CPU
  Input / output
  Memory
program
Instruction Memory
CPU
PC
ALU
A register
D register
Data
Data Memory
address
instruc-
tion
write
read
address

## Slide 85: Instruction memory
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Intro
  Computer architecture
  The Hack CPU
  Input / output
  Memory
program
ROM32K
CPU
PC
ALU
A register
D register
Data
Memory
address
instruc-
tion
write
read
address
0000000000001101
1110101001010101
0000000000000001
1110101001101011
0000001100110101
1110010111011111
.
.
.
1111001001100111
Hack Program
load
Hardware implementation
Plug-and-play ROM chip, named ROM32K
(pre-loaded with a program)
/** Read-Only memory (ROM),
acts as the Hack computer instruction memory. */
CHIP ROM32K {
IN address[15];
OUT out[16];
BUILTIN ROM32K;
}

## Slide 86: Instruction memory
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Intro
  Computer architecture
  The Hack CPU
  Input / output
  Memory
program
CPU
PC
ALU
A register
D register
Data
address
instruc-
tion
write
read
address
0000000000001101
1110101001010101
0000000000000001
1110101001101011
0000001100110101
1110010111011111
.
.
.
1111001001100111
Hack Program
load
Hardware simulation
Programs are stored in text files;
The simulator software features a load-program service.
ROM32K
Memory
Hardware implementation
Plug-and-play ROM chip, named ROM32K
(pre-loaded with a program)

## Slide 87: Chapter 5: Computer Architecture
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output

## Slide 88: Hack computer architecture
  Symbolic programming
  Control
  Variables
  Labels
  Overview
  Intro
  Computer architecture
  The Hack CPU
  Input / output
  Memory
program
CPU
PC
ALU
A register
D register
Data
address
instruc-
tion
write
read
address
Hello, world
Remaining challenge
Integrate into a single Computer chip
ROM32K
Memory

## Slide 89: Computer abstraction
Assumption:
The computer is loaded with a program written in the Hack machine language
reset
To execute the stored program:
set reset ← 1, then
set reset ← 0
Computer
like pushing and releasing a button

## Slide 90: Computer abstraction
if (reset == 1), executes the first instruction in the stored program
if (reset == 0), executes the next instruction in the stored program
Assumption:
The computer is loaded with a program written in the Hack machine language
reset
Computer abstraction:
like pushing and releasing a button
To execute the stored program:
set reset ← 1, then
set reset ← 0

## Slide 91: Computer implementation
reset

## Slide 92: Computer implementation
reset

## Slide 93: Computer implementation
reset

## Slide 94: Computer implementation
reset

## Slide 95: Computer implementation
reset

## Slide 96: Computer implementation
Hello, world
reset

## Slide 97: Computer implementation
Hello, world
reset

## Slide 98: Computer implementation
“Make everything as simple as possible, but no simpler.”
– Albert Einstein
Hello, world

## Slide 99: Chapter 5: Computer Architecture
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output

## Slide 100: Hack computer
Computer
Hello, world

## Slide 101: Hack computer
Hello, world

## Slide 102: CPU
/** Central Processing unit.
Executes instructions written in Hack machine language.
CHIP CPU {
Notes: Use built-in chip parts
It’s a very lean ALU, consisting of 2 registers, named D and A, a program counter, an ALU, and few more trivial gates.

## Slide 103: CPU
/** Central Processing unit.
Executes instructions written in Hack machine language.
CHIP CPU {
IN
inM[16], // Value of M (RAM[A])
instruction[16], // Instruction to execute
reset; // Signals whether to execute the first instruction
// (reset==1) or next instruction (reset == 0)
OUT
outM[16] // Value to write to the selected RAM register
writeM, // Write to the RAM?
addressM[15], // Address of the selected RAM register
pc[15]; // Address of the next instruction
PARTS:
// Put you code here:
}
Notes: Use built-in chip parts
It’s a very lean ALU, consisting of 2 registers, named D and A, a program counter, an ALU, and few more trivial gates.

## Slide 104: CPU implementation
Mux16
ALU
And, Or, Not ...
ARegister
DRegister
PC
Chip parts:
Built in project 1 and project 2
Built in project 3
ARegister and Dregister are built-in Register chips
Notes: Use built-in chip parts
It’s a very lean ALU, consisting of 2 registers, named D and A, a program counter, an ALU, and few more trivial gates.

## Slide 105: CPU implementation
Implementation
Use HDL to route instruction bits to chip-parts
Use gate logic to compute the address of the next instruction
Tips
No need for “helper chips”
Use logic gates and HDL for implementing everything.
1110011111010111
Notes: Use built-in chip parts
It’s a very lean ALU, consisting of 2 registers, named D and A, a program counter, an ALU, and few more trivial gates.

## Slide 106: Computer
Hello, world

## Slide 107: Memory
Memory
in
16
address
15
out
16
load
RAM16K
16383
0
Keyboard
24576
24575
16384
Screen
(8K memory map)
Memory.hdl
/** Complete address space of the computer’s data memory,
including RAM and memory mapped I/O.
Outputs the value of the memory location specified by address.
If (load==1), the in value is loaded into the memory location
specified by address.

## Slide 108: Memory
Memory
in
16
address
15
out
16
load
/** Complete address space of the computer’s data memory,
including RAM and memory mapped I/O.
Outputs the value of the memory location specified by address.
If (load==1), the in value is loaded into the memory location
specified by address.
Address space rules:
Only the upper 16K+8K+1 words of the memory are used.
Access to address 0 to 16383 results in accessing the RAM;
Access to address 16384 to 24575 results in accessing
the Screen memory map;
Access to address 24576 results in accessing the Keyboard
memory map.
*/
CHIP Memory {
IN address[15], in[16], load;
OUT out[16];
PARTS:
// Put your code here.
}
Memory.hdl
RAM16K
16383
0
Keyboard
24576
24575
16384
Screen
(8K memory map)

## Slide 109: Memory implementation
Memory
in
16
address
15
out
16
load
RAM16K
16383
0
Keyboard
24576
24575
16384
Screen
(8K memory map)
/** Memory of 16K 16-bit registers */
CHIP RAM16K {
IN
address[14], in[16], load;
OUT
out[16];
BUILTIN RAM16K;
CLOCKED in, load;
}
built in project 3
Implementation tip:
Use logic gates for mapping the address input on the corresponding address input of the relevant chip-part.
/** Memory of 8K 16-bit registers
with a display unit side effect. */
CHIP Screen {
IN
address[13], in[16], load;
OUT
out[16];
BUILTIN Screen;
CLOCKED in, load;
}
/** 16-bit register with a
keyboard input side effect */
CHIP Keyboard {
OUT
out[16];
BUILTIN Keyboard;
}

## Slide 110: Computer
reset

## Slide 111: Instruction memory
reset
ROM32K.hdl
/** Read-Only memory (ROM),
acting as the Hack computer instruction memory. */
CHIP ROM32K {
IN address[15];
OUT out[16];
BUILTIN ROM32K;
}

## Slide 112: Computer
reset

## Slide 113: Computer implementation
reset
Computer.hdl
/** The Hack computer, including CPU, RAM and ROM, loaded with a program.
When (reset==1), the computer executes the first instruction in the program;
When (reset==0), the computer executes the next instruction in the program. */
CHIP Computer {

## Slide 114: Computer implementation
reset
/** The Hack computer, including CPU, RAM and ROM, loaded with a program.
When (reset==1), the computer executes the first instruction in the program;
When (reset==0), the computer executes the next instruction in the program. */
CHIP Computer {
IN reset;
PARTS:
// Put your code here.
}
Computer.hdl

## Slide 115: Chapter 5: Computer Architecture
  Memory
  Computer
  Project 5: Chips
  Project 5: Guidelines
  Basic architecture
  Fetch-Execute cycle
  The Hack CPU
  Input / output

## Slide 116: Project 5
Build three chips:
Memory.hdl chip-parts: RAM16K, Screen, Keyboard
CPU.hdl chip-parts: ARgister, DRegister, PC, ALU, ...
Computer.hdl chip-parts: CPU, Memory, ROM32K
(All the chip-parts should be built-in chips, except for Memory and CPU)
Tools
Text editor
Hardware simulator

## Slide 117: Testing the Computer chip
reset
/** The Hack computer, including CPU, RAM and ROM, loaded with a program.
* When (reset==1), the computer executes the first instruction in the program;
* When (reset==0), the computer executes the next instruction in the program. */
CHIP Computer {
IN reset;
PARTS:
// Put your code here.
}
Computer.hdl
Testing logic:
Load Computer.hdl into the hardware simulator
Load a Hack program into the ROM32K chip-part
Run the clock enough cycles to execute the program

## Slide 118: Testing the Computer chip
Testing logic:
Load Computer.hdl into the hardware simulator
Load a Hack program into the ROM32K chip-part
Run the clock enough cycles to execute the program
Test programs
Add.hack: RAM[0] ← 2 + 3
Max.hack: RAM[2] ← max(RAM[0], RAM[1])
Rect.hack: Draws a rectangle of RAM[0] rows of 16 pixels each.

## Slide 119: Testing the Computer chip
Testing logic:
Load Computer.hdl into the hardware simulator
Load a Hack program into the ROM32K chip-part
Run the clock enough cycles to execute the program
Test programs
Add.hack: RAM[0] ← 2 + 3
Max.hack: RAM[2] ← max(RAM[0], RAM[1])
Rect.hack: Draws a rectangle of RAM[0] rows of 16 pixels each.
ComputerMax.tst
load Computer.hdl,
output-file ComputerMax.out,
compare-to ComputerMax.cmp,
output-list time reset ARegister[] DRegister[] PC[] RAM16K[0] RAM16K[1] RAM16K[2];
// Loads a Hack program (that executes R2 = max(R0,R1))
ROM32K load Max.hack,

## Slide 120: Testing the Computer chip
load Computer.hdl,
output-file ComputerMax.out,
compare-to ComputerMax.cmp,
output-list time reset ARegister[] DRegister[] PC[] RAM16K[0] RAM16K[1] RAM16K[2];
// Loads a Hack program (that executes R2 = max(R0,R1))
ROM32K load Max.hack,
// Test 1: computes max(3,5)
set RAM16K[0] 3,
set RAM16K[1] 5,
output;
repeat 14 {
tick, tock, output;
}
// Resets the PC
set reset 1,
tick, tock, output;
// Test 2: computes max(23456,12345)
set reset 0,
set RAM16K[0] 23456,
set RAM16K[1] 12345,
output;
repeat 14 {
tick, tock, output;
}
Testing logic:
Load Computer.hdl into the hardware simulator
Load a Hack program into the ROM32K chip-part
Run the clock enough cycles to execute the program
ComputerMax.tst
Test programs
Add.hack: RAM[0] ← 2 + 3
Max.hack: RAM[2] ← max(RAM[0], RAM[1])
Rect.hack: Draws a rectangle of RAM[0] rows of 16 pixels each.

## Slide 121: Testing the Computer chip
Testing logic:
Load Computer.hdl into the hardware simulator
Load a Hack program into the ROM32K chip-part
Run the clock enough cycles to execute the program
Rect.hack output:
R0
Test script
ComputerRect.tst
Inspect it, and understand the testing logic.
Test programs
Add.hack: RAM[0] ← 2 + 3
Max.hack: RAM[2] ← max(RAM[0], RAM[1])
Rect.hack: Draws a rectangle of RAM[0] rows of 16 pixels each.

## Slide 122: What’s next?
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
p4
Writing low-level programs
p5
This chapter

## Slide 123: What’s next?
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
Developing an assembler
p2
p3
p1
p4
Writing low-level programs
p5
p6
Next chapter

## Slide 124: End note: Memory hierarchy
Memory
CPU
ALU
register
register
register






Challenges
Slow access time
Limited memory space
instructions, data
addresses, data
Separate chips, bits travel long distances
Notes: Accessing a memory location is expensive
  Need to supply a long address
  Getting the memory contents into the CPU takes time

## Slide 125: End note: Memory hierarchy
Memory
CPU
ALU
register



Mass Storage
register
register






Cache
Challenges
Slow access time
Limited memory space
Typical solutions
Cache memory
External storage

## Slide 126: End note: Memory hierarchy
Memory
CPU
ALU
register



Mass Storage
more storage space, slower access time
register
register






Cache
Memory hierarchy:

## Slide 127: End note: Memory hierarchy
Memory
CPU
ALU
register



Mass Storage
register
register






Cache
Mass storage and cache memory are possible extensions
The basic Hack computer is built without them.