## Slide 1
Chapter 6
Assembler
From Nand to Tetris
Building a Modern Computer from First Principles
These slides support chapter 6 of the book
The Elements of Computing Systems
(1st and 2nd editions)
By Noam Nisan and Shimon Schocken
MIT Press

## Slide 2: Usage Notice
  You are welcome to use this presentation, or any part of it, in Nand to Tetris courses, or in other courses, as you see fit.
  Usage is free provided that it supports instruction in educational, non-profit settings.
  You can use the slides as-is, or modify them as needed.
  We’ll appreciate it if you will credit Nand to Tetris somewhere, and put a reference to www.nand2tetris.org
  Happy teaching!
  Shimon Schocken / Noam Nisan

## Slide 3: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
p2
p3
p1
p4
Writing low-level programs
p5
assembler
Assembler: A program that translates symbolic machine language programs to binary code that can be executed by the computer

## Slide 4: Nand to Tetris Roadmap (Part I: Hardware)
abstraction
computer
abstraction
ALU, RAM
abstraction
elementary logic gates
abstraction
Nand
Building gates
machine language
hardware platform
Building chips
Building a computer
p2
p3
p1
p4
Writing low-level programs
p5
p6
Developing the assembler
assembler
This chapter

## Slide 5: The assembler
load and execute
// Program: Sum1ToN (R0 represents N)
// Computes R1 = 1 + 2 + 3 + ... + R0
// Usage: put a value >= 1 in R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if (i > R0) goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum = sum + i
@sum
D=M
@i
D=D+M
@sum
M=D
// i = i + 1
@i
M=M+1
// goto LOOP
@LOOP
0;JMP
...
0101111100111100
1010101010101010
1100000010101010
1011000010000001
0101111100111100
1010101010101010
1100000010101010
0101111100111100
1010101010101010
1100000010101010
1011000010000001
0101111100111100
1010101010101010
1100000010101010
0101111100111100
1010101010101010
1100000010101010
1011000010000001
0101111100111100
1010101010101010
1100000010101010
...
Binary code
assembler
Symbolic low-level program
Computer
Why write an assembler?
Because it is the “linchpin” that connects the hardware platform and the software hierarchy that sits on top of it
Because it provides a simple example of key software engineering techniques (parsing, code generation, symbol tables, …)

## Slide 6: Chapter 6: Assembler
  Overview
  Translating instructions
  Translating programs
  Handling symbols
  Assembler architecture
  Assembler API
  Project 6
  Some history

## Slide 7: Chapter 6: Assembler
  Overview
  Translating instructions
    A-instructions
    C-instructions
  Translating programs
  Handling symbols
  Assembler architecture
  Assembler API
  Project 6
  Some history

## Slide 8: Translating A-instructions
Where xxx is a non-negative decimal value, or a symbol bound to such a value
Binary syntax:
0vvvvvvvvvvvvvvvv
@xxx
Symbolic syntax:
Where:
  0 is the A-instruction op-code, and
  v v v … v is the value in binary
translate
Implementation
Simple: Translate the decimal value into its 16-bit representation.
0000000000010001
@17
Example:
becomes

## Slide 9: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump

## Slide 10: Translating C-instructions
Implementation: Simple: Translate each field of the symbolic instruction (dest, comp, jump) into its binary code, and assemble the codes into a 16-bit instruction.
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump

## Slide 11: Translating C-instructions
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
Binary:
Example:
D=D+1;JLE

## Slide 12: Translating C-instructions
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
111
Binary:
D=D+1;JLE
Example:

## Slide 13: Translating C-instructions
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
111
Binary:
D=D+1;JLE
Example:

## Slide 14: Translating C-instructions
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111
Binary:
D=D+1;JLE
Example:

## Slide 15: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111
Binary:
D=D+1;JLE
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 16: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111
Binary:
D=D+1;JLE
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 17: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111010
Binary:
D=D+1;JLE
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 18: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111010
Binary:
D=D+1;JLE
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 19: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111010
Binary:
D=D+1;JLE
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 20: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111010110
Binary:
D=D+1;JLE
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 21: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110011111010110
Binary:
D=D+1;JLE
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 22: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
Binary:
A=-1
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 23: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
111
Binary:
A=-1
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 24: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
111
Binary:
A=-1
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 25: Translating C-instructions
Symbolic syntax:
1 1 1 a c c c c c c d d d j j j
Binary syntax:
dest = comp ; jump
1110111010100000
Binary:
A=-1
comp |  | c | c | c | c | c | c
0 |  | 1 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 1 | 1 | 1 | 1 | 1
-1 |  | 1 | 1 | 1 | 0 | 1 | 0
D |  | 0 | 0 | 1 | 1 | 0 | 0
A | M | 1 | 1 | 0 | 0 | 0 | 0
!D |  | 0 | 0 | 1 | 1 | 0 | 1
!A | !M | 1 | 1 | 0 | 0 | 0 | 1
-D |  | 0 | 0 | 1 | 1 | 1 | 1
-A | -M | 1 | 1 | 0 | 0 | 1 | 1
D+1 |  | 0 | 1 | 1 | 1 | 1 | 1
A+1 | M+1 | 1 | 1 | 0 | 1 | 1 | 1
D-1 |  | 0 | 0 | 1 | 1 | 1 | 0
A-1 | M-1 | 1 | 1 | 0 | 0 | 1 | 0
D+A | D+M | 0 | 0 | 0 | 0 | 1 | 0
D-A | D-M | 0 | 1 | 0 | 0 | 1 | 1
A-D | M-D | 0 | 0 | 0 | 1 | 1 | 1
D&A | D&M | 0 | 0 | 0 | 0 | 0 | 0
D¦A | D¦M | 0 | 1 | 0 | 1 | 0 | 1
a==0 | a==1 |  |  |  |  |  | 
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]
Example:

## Slide 26: Chapter 6: Assembler
  Overview
  Translating instructions
  Translating programs
  Handling symbols
  Assembler architecture
  Assembler API
  Project 6
  Some history

## Slide 27: Program translation
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Translate
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
...
Binary code
Need to handle:
White space
Instructions
Symbols
We’ll start with programs that have no symbols,
and handle symbols later

## Slide 28: Program translation
Need to handle:
White space
Instructions
Symbols (later)
Translate
Binary code
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@16
M=1
// sum = 0
@17
M=0
// if i>R0 goto STOP
@16
D=M
@0
D=D-M
@18
D;JGT
// sum += i
@16
D=M
@17
M=D+M
// i++
@16
M=M+1
@4
0;JMP
@17
D=M
...
no symbols

## Slide 29: Program translation
Translate
Binary code
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@16
M=1
// sum = 0
@17
M=0
// if i>R0 goto STOP
@16
D=M
@0
D=D-M
@18
D;JGT
// sum += i
@16
D=M
@17
M=D+M
// i++
@16
M=M+1
@4
0;JMP
@17
D=M
...
no symbols
Need to handle:
White space
Instructions
Symbols (later)

## Slide 30: Program translation
Need to handle:
White space
Instructions
Symbols (later)
Translate
Binary code
// Computes R1=1 + ... + R0
// i = 1
@16
M=1
// sum = 0
@17
M=0
// if i>R0 goto STOP
@16
D=M
@0
D=D-M
@18
D;JGT
// sum += i
@16
D=M
@17
M=D+M
// i++
@16
M=M+1
@4
0;JMP
@17
D=M
...
Symbolic code
Ignore it
no symbols
White space:
Empty lines,
Comments,
Indentation

## Slide 31: Program translation
Need to handle:
White space
Instructions
Symbols (later)
Translate
Binary code
Symbolic code
no symbols
@16
M=1
@17
M=0
@16
D=M
@0
D=D-M
@18
D;JGT
@16
D=M
@17
M=D+M
@16
M=M+1
@4
0;JMP
@17
D=M
...

## Slide 32: Program translation
Need to handle:
White space
Instructions
Symbols (later)
Translate
Binary code
Symbolic code
no symbols
@16
M=1
@17
M=0
@16
D=M
@0
D=D-M
@18
D;JGT
@16
D=M
@17
M=D+M
@16
M=M+1
@4
0;JMP
@17
D=M
...
Translate, one by one

## Slide 33: Program translation
Translate
Binary code
Translate, one by one
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
...
Symbolic code
no symbols
@16
M=1
@17
M=0
@16
D=M
@0
D=D-M
@18
D;JGT
@16
D=M
@17
M=D+M
@16
M=M+1
@4
0;JMP
@17
D=M
...
Need to handle:
White space
Instructions
Symbols (later)

## Slide 34: Program translation
Need to handle:
White space
Instructions
Symbols
Translate
Binary code
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
...
Symbolic code
no symbols
@16
M=1
@17
M=0
@16
D=M
@0
D=D-M
@18
D;JGT
@16
D=M
@17
M=D+M
@16
M=M+1
@4
0;JMP
@17
D=M
...

## Slide 35: Program translation
Need to handle:
White space
Instructions
Symbols
Translate
Binary code
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
...
Symbolic code
no symbols
@16
M=1
@17
M=0
@16
D=M
@0
D=D-M
@18
D;JGT
@16
D=M
@17
M=D+M
@16
M=M+1
@4
0;JMP
@17
D=M
...

## Slide 36: Program translation
Translate
Binary code
no symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Original program, with symbols
Need to handle:
White space
Instructions
Symbols

## Slide 37: Handling symbols
Symbolic code
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols
Original program, with symbols

## Slide 38: Handling symbols
Symbolic code
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols
Original program, with symbols

## Slide 39: Handling symbols
Symbolic code
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols
This particular program uses one predefined symbol: R0

## Slide 40: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
The Hack language features 23 predefined symbols:
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
SCREEN | 16384
KBD | 24576
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
This particular program uses one predefined symbol: R0

## Slide 41: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Translating @preDefinedSymbol :
Replace preDefinedSymbol with its value
The Hack language features 23 predefined symbols:
@R15
0000000000001111
Example:
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
SCREEN | 16384
KBD | 24576
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4

## Slide 42: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols

## Slide 43: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols

## Slide 44: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols
This particular program uses two label symbols: LOOP, STOP

## Slide 45: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Label symbols
Used to label destinations of goto instructions
Declared by the pseudo-instruction (label)
The (label) directive defines the symbol label to refer to the memory location holding the next instruction in the program,
Which corresponds to the instruction’s line number
This particular program uses two label symbols: LOOP, STOP

## Slide 46: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
...
Label symbols
Used to label destinations of goto instructions
Declared by the pseudo-instruction (label)
The (label) directive defines the symbol label to refer to the memory location holding the next instruction in the program,
Which corresponds to the instruction’s line number
This particular program uses two label symbols: LOOP, STOP

## Slide 47: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
symbol | value
LOOP | 4
STOP | 18
Example:
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
...
Label symbols
Used to label destinations of goto instructions
Declared by the pseudo-instruction (label)
The (label) directive defines the symbol label to refer to the memory location holding the next instruction in the program,
Which corresponds to the instruction’s line number
This particular program uses two label symbols: LOOP, STOP

## Slide 48: Handling symbols
Symbolic code
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
...
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Translating @labelSymbol :
Replace labelSymbol with its value
@LOOP
0000000000000100
Example:
symbol | value
LOOP | 4
STOP | 18
Example:
Label symbols
Used to label destinations of goto instructions
Declared by the pseudo-instruction (label)
The (label) directive defines the symbol label to refer to the memory location holding the next instruction in the program,
Which corresponds to the instruction’s line number

## Slide 49: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols

## Slide 50: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbols
Predefined symbols
Label symbols
Variable symbols

## Slide 51: Handling symbols
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Symbolic code
Symbols
Predefined symbols
Label symbols
Variable symbols
This particular program uses two variable symbols: i, sum

## Slide 52: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Variable symbols
Any symbol xxx which is neither predefined, nor defined elsewhere using an (xxx) label declaration, is treated as a variable
Each variable is bound to a running memory address, starting at 16
This particular program uses two variable symbols: i, sum

## Slide 53: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Example:
symbol | value
i | 16
sum | 17
This particular program uses two variable symbols: i, sum
Variable symbols
Any symbol xxx which is neither predefined, nor defined elsewhere using an (xxx) label declaration, is treated as a variable
Each variable is bound to a running memory address, starting at 16

## Slide 54: Handling symbols
symbol | value
i | 16
sum | 17
Translating @variableSymbol :
If variableSymbol is seen for the first time, bind to it a value, from 16 onward
Else, it has a value
Replace variableSymbol with its value.
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
@sum
0000000000010001
Example:
Example:
Variable symbols
Any symbol xxx which is neither predefined, nor defined elsewhere using an (xxx) label declaration, is treated as a variable
Each variable is bound to a running memory address, starting at 16

## Slide 55: Handling symbols
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
SCREEN | 16384
KBD | 24576
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
LOOP | 4
STOP | 18
i | 16
sum | 17
Symbol table
A data structure that the assembler creates and uses during the program translation
Contains the predefined symbols, label symbols, variable symbols, And their bindings.

## Slide 56: Handling symbols
symbol | value
Symbol table
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
A data structure that the assembler creates and uses during the program translation

## Slide 57: Handling symbols
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
SCREEN | 16384
KBD | 24576
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
Symbol table
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Initialization: Creates the table and adds all the predefined symbols
A data structure that the assembler creates and uses during the program translation

## Slide 58: Handling symbols
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
SCREEN | 16384
KBD | 24576
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
LOOP | 4
STOP | 18
Symbol table
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
...
Initialization: Creates the table and adds all the predefined symbols
First pass: Counts lines and adds the label symbols
A data structure that the assembler creates and uses during the program translation

## Slide 59: Handling symbols
symbol | value
R0 | 0
R1 | 1
R2 | 2
... | ...
R15 | 15
SCREEN | 16384
KBD | 24576
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
LOOP | 4
STOP | 18
i | 16
sum | 17
Symbol table
Second pass: Generates binary code; In the process, adds the variable symbols
(details, soon)
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Initialization: Creates the table and adds all the predefined symbols
First pass: Counts lines and adds the label symbols
A data structure that the assembler creates and uses during the program translation

## Slide 60: Translating programs
Symbolic code
// Computes R1=1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i>R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
// sum += i
@i
D=M
@sum
M=D+M
// i++
@i
M=M+1
@LOOP
0;JMP
(STOP)
@sum
D=M
...
Need to handle:
White space
Instructions
Symbols
Translate
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
...
Binary code

## Slide 61: Chapter 6: Assembler
  Overview
  Translating instructions
  Translating programs
  Handling symbols
  Assembler architecture
  Assembler API
  Project 6
  Some history

## Slide 62: Assembler: Usage
Input (Prog.asm): a text file containing a sequence of lines, each being a comment, an A instruction, or a C-instruction
Output (Prog.hack): a text file containing a sequence of lines, each being a string of sixteen 0 and 1 characters
Usage: (if the assembler is implemented in Java)
$ java HackAssembler Prog.asm
Action: Creates a Prog.hack file, containing the translated Hack program

## Slide 63: Assembler: Algorithm
Assembler implementation options
Manual
Program-based
Initialize:
Opens the input file (Prog.asm), and gets ready to process it
Constructs a symbol table, and adds to it all the predefined symbols
First pass:
Reads the program lines, one by one, focusing only on (label) declarations. Adds the found labels to the symbol table
Second pass (main loop):
(starts again from the beginning of the file)
While there are more lines to process:
Gets the next instruction, and parses it
If the instruction is @symbol
    If symbol is not in the symbol table, adds it
    Translates the symbol to its binary value
If the instruction is dest=comp;jump
    Translates each of the three fields into its binary value
Assembles the binary values into a string of sixteen 0’s and 1’s
Writes the string to the output file.

## Slide 64: Assembler: Architecture
Parser
Code
SymbolTable
reads and parses an instruction
generates binary code
handles symbols
Proposed architecture
Four software modules
Can be realized in any programming language
HackAssembler
drives the translation process

## Slide 65: HackAssembler
The HackAssembler implements the assembly algorithm, using the services of:
Parser
Code
SymbolTable
Initialize:
Opens the input file (Prog.asm) and gets ready to process it
Constructs a symbol table, and adds to it all the predefined symbols
First pass:
Reads the program lines, one by one focusing only on (label) declarations. Adds the found labels to the symbol table
Second pass (main loop):
(starts again from the beginning of the file)
While there are more lines to process:
Gets the next instruction, and parses it
If the instruction is @symbol
    If symbol is not in the symbol table, adds it
    Translates the symbol into its binary value
If the instruction is dest=comp;jump
    Translates each of the three fields into its binary value
Assembles the binary values into a string of sixteen 0’s and 1’s
Writes the string to the output file.

## Slide 66: Assembler API
Parser
Code
SymbolTable
reads and parses an instruction
generates binary code
handles symbols
HackAssembler
drives the process

## Slide 67: Parser API
Routines:
Constructor / initializer: Creates a Parser and opens the source text file
Getting the current instruction:
  hasMoreLines(): Checks if there is more work to do (boolean)
  advance(): Gets the next instruction and makes it the current instruction (string)
Parsing the current instruction:
  instructionType(): Returns the current instruction type (constant):
  A_INSTRUCTION for @xxx, where xxx is either a decimal number or a symbol
  C_INSTRUCTION for dest=comp;jump
  L_INSTRUCTION for (label)
D=0
(END)
instructionType() returns C_INSTRUCTION
instructionType() returns L_INSTRUCTION
@17
instructionType() returns A_INSTRUCTION
Examples:
current instruction
@sum
instructionType() returns A_INSTRUCTION

## Slide 68: Parser API
Routines:
Constructor / initializer: Creates a Parser and opens the source text file
Getting the current instruction:
  hasMoreLines(): Checks if there is more work to do
  advance(): Gets the next instruction and makes it the current instruction
Parsing the current instruction:
  instructionType(): Returns the instruction type

## Slide 69: Parser API
Routines:
Constructor / initializer: Creates a Parser and opens the source text file
Getting the current instruction:
  hasMoreLines(): Checks if there is more work to do
  advance(): Gets the next instruction and makes it the current instruction
Parsing the current instruction:
  instructionType(): Returns the instruction type
  symbol(): Returns the instruction’s symbol (string)
Used if the current instruction is @symbol or (symbol)
Examples:
current instruction
@sum
(LOOP)
symbol() returns "sum"
symbol() returns "LOOP"

## Slide 70: Parser API
Routines:
Constructor / initializer: Creates a Parser and opens the source text file
Getting the current instruction:
  hasMoreLines(): Checks if there is more work to do
  advance(): Gets the next instruction and makes it the current instruction
Parsing the current instruction:
  instructionType(): Returns the instruction type
  symbol(): Returns the instruction’s symbol (string)

## Slide 71: Parser API
Routines:
Constructor / initializer: Creates a Parser and opens the source text file
Getting the current instruction:
  hasMoreLines(): Checks if there is more work to do
  advance(): Gets the next instruction and makes it the current instruction
Parsing the current instruction:
  instructionType(): Returns the instruction type
  symbol(): Returns the instruction’s symbol (string)
  dest(): Returns the instruction’s dest field (string)
  comp(): Returns the instruction’s comp field (string)
  jump(): Returns the instruction’s jump field (string)
Used if the current instruction is dest=comp;jump
D=D+1;JLE
Examples:
current instruction
dest() returns "D"
comp() returns "D+1"
jump() returns "JLE"
M=-1
dest() returns "M"
comp() returns "-1"
jump() returns null

## Slide 72: Implementation
Parser
Code
SymbolTable
reads and parses an instruction
generates binary code
handles symbols
HackAssembler
drives the process

## Slide 73: Code API
Deals only with C-instructions: dest = comp ; jump
Routines:
dest(string): Returns the binary representation of the parsed dest field (string)
comp(string): Returns the binary representation of the parsed comp field (string)
jump(string): Returns the binary representation of the parsed jump field (string)
According to the language specification:
dest("DM") returns "011"
Examples:
comp("A+1") returns "0110111"
comp("D&M") returns "1000000"
jump("JNE") returns "101"

## Slide 74: Implementation
Parser
Code
SymbolTable
reads and parses an instruction
generates binary code
handles symbols
HackAssembler
drives the process

## Slide 75: SymbolTable API
Routines
Constructor / initializer: Creates and initializes a SymbolTable
addEntry(symbol (string), address (int)): Adds <symbol, address> to the table (void)
contains(symbol (string)): Checks if symbol exists in the table (boolean)
getAddress(symbol (string)): Returns the address (int) associated with symbol
Symbol table: (example)

## Slide 76: HackAssembler: Drives the translation process
Parser
Code
SymbolTable
reads and parses an instruction
generates binary code
handles symbols
HackAssembler
drives the process

## Slide 77: Assembler API (detailed)
Parser module:

## Slide 78: Assembler API (detailed)
Code module:
SymbolTable module:
HackAssembler module:
We propose no API; Implement as you see fit.

## Slide 79: Chapter 6: Assembler
  Overview
  Translating instructions
  Translating programs
  Handling symbols
  Assembler architecture
  Assembler API
  Project 6
  Some history

## Slide 80: Developing a Hack Assembler
Contract
Develop a program that translates symbolic Hack programs into binary Hack instructions
The source program (input) is supplied as a text file named Prog.asm
The generated code (output) is written into a text file named Prog.hack
Assumption: Prog.asm is error-free
Usage (if the assembler is implemented in Java):
$ java HackAssembler Prog.asm
Staged development plan
Develop a basic assembler that translates programs that have no symbols
Develop an ability to handle symbols
Morph the basic assembler into an assembler that translates any program

## Slide 81: Testing
// Computes R1 = 1 + ... + R0
// i = 1
@i
M=1
// sum = 0
@sum
M=0
(LOOP)
// if i > R0 goto STOP
@i
D=M
@R0
D=D-M
@STOP
D;JGT
...
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
...
Prog.hack
Prog.asm
Your
assembler
Load /
Run
Or use a supplied test script that loads Prog.hack into the CPU emulator and tests it using pre-defined testing scenarios
Test programs
Add.asm
Max.asm
Rect.asm
Pong.asm
(same programs, without symbols, for unit-testing the basic assembler)
(with symbols)
MaxL.asm
RectL.asm
PongL.asm
CPU Emulator

## Slide 82: Testing
// Computes RAM[0] =
// 2 + 3
@2
D=A
@3
D=D+A
@0
M=D
Add.asm
Testing on the CPU emulator:
1. Translate Add.asm using your assembler
2. Load the translated Add.hack
3. Run the code, inspect R0.
Note: When loading a binary Prog.hack file into the CPU emulator, the emulator may translate it back to symbolic code (depending on the emulator’s version).
To inspect the binary code, select this option from the ROM menu.

## Slide 83: Testing
// Computes RAM[2] =
// max(RAM[0],RAM[1])
@R0
D=M
@R1
D=D-M
@OUTPUT_RAM0
D;JGT
// Output RAM[1]
@R1
D=M
@R2
M=D
@END
0;JMP
(OUTPUT_RAM0)
@R0
D=M
@R2
M=D
(END)
@END
0;JMP
Max.asm
Testing on the CPU emulator:
Translate and load, then:
Put test values in R0 and R1, run the code, inspect R2.

## Slide 84: Testing
// Computes RAM[2] =
// max(RAM[0],RAM[1])
@R0
D=M
@R1
D=D-M
@OUTPUT_RAM0
D;JGT
// Output RAM[1]
@R1
D=M
@R2
M=D
@END
0;JMP
(OUTPUT_RAM0)
@R0
D=M
@R2
M=D
(END)
@END
0;JMP
Max.asm
with symbols
without symbols
// Computes RAM[2] =
// max(RAM[0],RAM[1])
@0
D=M
@1
D=D-M
@12
D;JGT
// Output RAM[1]
@1
D=M
@2
M=D
@16
0;JMP
@0
D=M
@2
M=D
@16
0;JMP
MaxL.asm
For unit-testing the basic assembler
(Each symbol was replaced with its value)

## Slide 85: Testing
// Draws a rectangle.
@R0
D=M
@n
M=D
@i
M=0
@SCREEN
D=A
@address
M=D
(LOOP)
@i
D=M
@n
D=D-M
@END
D;JGT
...
Rect.asm
Draws a rectangle, 16 pixels wide and R0 lines high
Testing on the CPU emulator:
Translate and load, then:
Put a non-negative value in R0, run the code, inspect the screen.

## Slide 86: Testing
// Draws a rectangle.
@0
D=M
@16
M=D
@17
M=0
@16384
D=A
@18
M=D
(LOOP)
@17
D=M
@16
D=D-M
@27
D;JGT
...
RectL.asm
without symbols
// Draws a rectangle.
@R0
D=M
@n
M=D
@i
M=0
@SCREEN
D=A
@address
M=D
(LOOP)
@i
D=M
@n
D=D-M
@END
D;JGT
...
Rect.asm
with symbols
For unit-testing the basic assembler

## Slide 87: Testing
// Pong.asm
@256
D=A
@SP
M=D
@133
0;JMP
@R15
M=D
@SP
AM=M-1
D=M
A=A-1
D=M-D
M=0
@END_EQ
D;JNE
@SP
A=M-1
M=-1
(END_EQ)
@R15
A=M
...
Pong.asm
Translate and load, and then play the game:
Select “no animation”, set the speed slider to “fast”, and run the code. Move the paddle using the left- and right-arrow keys.
Pong game

## Slide 88: Testing
// Pong.asm
@256
D=A
@SP
M=D
@133
0;JMP
@R15
M=D
@SP
AM=M-1
D=M
A=A-1
D=M-D
M=0
@END_EQ
D;JNE
@SP
A=M-1
M=-1
(END_EQ)
@R15
A=M
...
Pong.asm
Background
The original Pong program was written in the high-level Jack language
The computer’s operating system is also written in Jack
The Pong code + the OS code were compiled by the Jack compiler, creating a single Pong.asm file
The compiled code (Pong.asm) has:
No white space, and
Compiler-generated addresses and symbols (which may look strange)
28,374 instructions

## Slide 89: Testing option II: Using the hardware simulator
Use your assembler to translate Prog.asm, generating the executable file Prog.hack
Put the Prog.hack file in a folder containing the chips that you developed in project 5: Computer.hdl, CPU.hdl, and Memory.hdl
Load Computer.hdl into the Hardware Simulator
Load Prog.hack into the ROM32K chip-part
Run the clock to execute the program.

## Slide 90: Testing option III: Using the supplied assembler
Source Prog.asm test file
Prog.hack file, translated by your assembler
Prog.hack file, translated by the supplied assembler
Use your assembler to translate Prog.asm, generating the executable file Prog.hack
Load Prog.asm into the supplied assembler, and load Prog.hack as a compare file
Translate Prog.hack, and inspect the comparison feedback messages.

## Slide 91: Project 6
Guidelines: www.nand2tetris.org (projects section)
Files: nand2tetris/projects/06 (on your PC)
Tools
  The programming language in which you develop your assembler
  CPU emulator (for testing the translated programs)
  Assembler (if you plan to use it)
Guides
  CPU emulator tutorial
  Assembler tutorial

## Slide 92: Chapter 6: Assembler
  Overview
  Translating instructions
  Translating programs
  Handling symbols
  Assembler architecture
  Assembler API
  Project 6
  Some history

## Slide 93: The Industrial Revolution (1760 – 1840) / Case in Point: Textile
Cotton picking
cleaning
spinning
weaving
  Until 1800: labor intensive / slavery / child labor
  Industrial revolution: all key processes are mechanized.

## Slide 94: The Industrial Revolution (1760 – 1840) / Case in Point: Textile
Jacquard loom (1801)
  The weaving instructions were programmed by punched cards
  The cards coded instructions for the loom’s hardware.

## Slide 95: The Industrial Revolution (1760 – 1840) / Case in Point: Textile
  The weaving instructions were programmed by punched cards
  The cards coded instructions for the loom’s hardware.

## Slide 96: The Analytic Engine (1837)
An early mechanical computer, designed by Charles Babbage
Designed to tabulate data collected in a UK national census
Featured a simple programming model with conditional branching
Software = punched cards

## Slide 97: Ada Lovelace (1815 – 1852)
Ada’s insight:
If you want to give a computer instructions, don’t start by punching cards (“binary code”)
Instead, write the instructions on paper, using a symbolic language
When convinced that the symbolic program is error-free, translate it into punched cards.
Ada Augusta King-Noel, Countess of Lovelace
Gifted mathematician and writer
Worked closely with Babbage on the Analytic Engine.

## Slide 98: Ada Lovelace (1815 – 1852)
Often described as “the first programmer”
The programming language Ada is named after her.
Early program, written by Ada, to compute Bernoulli numbers on the Analytic Engine

## Slide 99: Ada Lovelace (1815 – 1852)
“The Analytical Engine might act upon other things besides numbers...
Suppose, for instance, that the fundamental relations of pitched sounds in the science of harmony and of musical composition were susceptible of such expression and adaptations...
If so, the engine might compose elaborate and scientific pieces of music of any degree of complexity.”
(1840!)